DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS JANUARY 25, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 251 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 175 | 175 |
| CAMERON | 1726 | 1726 |
| HALLIBURTON | 3530 | 3530 |
| SCHLUMBERGER | 2435 | 2435 |
| ISS | 243 | 2357 |

Well: HLA_A4

Rig/Contractor: 	Rig 453	Report Date: January 25, 2007

Supervisor:	Stead, Cory

Steel, George A

| AFE Number: AFE Number: | L0501H209 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 1.0 | AFE Cost/Days: | $800,000 |
| Daily Cost: | $195,848 |  |  |
| Total Cost: | $195,848 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A4 |
| --- | --- |
| Management Summary: | Prepare & skid rig to HLA A4 for slickline job. Reinstate access ways, landings & stairways. Service MV Far Scandia - offload deck panels, bulks & mud chemicals. Spot deck panels in place. |
| Current: | Reinstating access ways & services. |
| Planned: | R/U slickline. RIH & pull SSSV @ 132.4m & B-mandrel @ 775.5m. Set x-plug @ 1453m. Run gyro survey. Set dummy mandrel @ 775.5m. Test plugs to 1000 psi. Set FSE SSSV & BPV. R/dn slickline. |