DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS August 15, 2006

SAFETY

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| RIG 453 | 289 | 363 |
| --- | --- | --- |
| CAMERON | 5542 | 5541 |
| HALLIBURTON | 3364 | 3363 |
| SCHLUMBERGER | 2144 | 21 |
| ISDL | 289 | 647 |
| ISS | 77 | 2364 |

Well: WKF_W21

Rig/Contractor: 	Rig 453	Report Date: August 15, 2006

Supervisor:	Campbell, Glen R

Davis, Brian

| AFE Number: | 40000458 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 7.2 | AFE Cost/Days: | $1,783,661 |
| Daily Cost: | $185,329 |  |  |
| Total Cost: | $1,326,429 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: | 633.00 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W21 |
| --- | --- |
| Management Summary: | WOC. RIH & tag cmt. Wash to 653m. Test csg to 1000 psi/no test. Rev circ. Respond to ERA. RIH to 652m. Set cement plug #4. POH to 605m & rev circ. POH to surface. Rig serv. R/up Anadrill. M/up 8½" BHA. Test csg to 1000 psi. |
| Current: | Change UPR's & MPR's. Change over to drilling AFE. |
| Planned: | Change & pressure test rams. Commence drilling program. |