Report for : Richard Moore / Mark Calicutt / Andy Choy

Compiled by  : Col Chadwick

| WELL | CBA-A21A |
| --- | --- |
| DATE | 21-03-2009 |
| REPORT # | 07 |
| MIDNIGHT ACTIVITY | Drilling ahead 97/8" hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3500.0 mMDRT |  | MINIMUM | 17.76 | 3268.0 |
| TVD | 2249.73 mTVDRT |  | MAXIMUM | 94.95 | 2801.0 |
| PROGRESS LAST 24 hrs | 769.0 m |  | AVERAGE | 51.95 | 2731-3500m |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 3390.0 | 2185.9 | -2144.9 | 12.1 H | 3406.0 | 2198.0 |
| Top of Latrobe Grp |  |  |  |  | 3648.0 | 2330.0 |
| Top Coarse Clastics / M111 Reservoir |  |  |  |  | 3656.0 | 2334.0 |
| Top M112 Reservoir |  |  |  |  | 3689.9 | 2351.0 |
| Top M131 Reservoir |  |  |  |  | 3699.9 | 2356.0 |
| Top M132 Upper Reservoir |  |  |  |  | 3733.8 | 2373.0 |
| Top M132 Lower Reservoir |  |  |  |  | 3741.8 | 2377.0 |
| 4AFS Marker |  |  |  |  | 3763.8 | 2388.0 |
| M145 Reservoir |  |  |  |  | 3791.7 | 2402.0 |
| Halibut Org OWC |  |  |  |  | 3863.5 | 2438.0 |
| Total Depth |  |  |  |  | 3903.5 | 2458.0 |

| Current Formation | Gippsland Limestone: Calcilutite |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2871.0 | 24.00 | 0.461 | 0.004 | 0.002 | 0.002 | 0.001 | - |
| MAX (GFF) | 2922.0 | 21.00 | 0.541 | 0.003 | 0.000 | 0.000 | 0.000 | - |
| BG (Reserval) | 2731.0-3500.0 | 15.77 | 0.309 | 0.003 | 0.001 | 0.002 | 0.001 | - |
| BG (GFF) | 2731.0-3500.0 | 11.97 | 0.190 | 0.001 | 0.028 | 0.017 | 0.000 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 | - |
| SIZE (in) | 97/8" | - |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 | - |
| JETS (/32 inch) | 6 x 18 | - |
| DEPTH IN (m) | 638.0 | - |
| DEPTH OUT (m) | - | - |
| METRES ON RUN (m) | 2862.0 | - |
| HRS ON BTM 24hrs/total | 14.8 / 80.7 | - |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 111-165 | - |
| Pump Hrs 24 hrs / total | 21.4 / 113.8 | - |
| Krevs 24 hrs / total | 114 / 528 | - |

| 24 HOUR SUMMARY | Drill, steer and survey 97/8" hole from 2731.0 mMDRT to 3353.0 mMDRT. Circulate and condition hole clean while fixing SCOMI mud drier. Drill, steer and survey 97/8" hole from 3353.0 mMDRT to 3411.0 mMDRT. Circulate and condition hole clean while fixing SCOMI mud drier. Drill, steer and survey 97/8" hole from 3411.0 mMDRT to 3500.0 mMDRT. |
| --- | --- |
| 22-03-2009 5AM UPDATE | Drill, steer and survey 97/8" hole from 3500.0 mMDRT to 3617.0 mMDRT. Circulate and condition hole clean from 3589.0 mMDRT to 3617.0 mMDRT. 3617.0 mMDRT (2313.89 mTVDRT) |