Report for : Sam Falkner / Greg Doty / Richard Moore

Compiled by : Gareth Munro

| WELL | CBA A33 |
| --- | --- |
| DATE | 23-06-2009 |
| REPORT # | 10 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2329.00 mMDRT |  | MINIMUM | 32.19 | 2017.0 |
| TVD | 2261.01 mMDRT |  | MAXIMUM | 146.71 | 1186.0 |
| PROGRESS LAST 24 hrs | 1321 m |  | AVERAGE | 83.6 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 2233.0 | 2168.2 | -2127.2 | 22.8mH | 2255.0 | 2191.0 |
| Top of Latrobe Group | 2462.0 | 2389.3 | -2348.3 | 5.7mH | 2466.0 | 2395.0 |
| Top Coarse Clastics | 2464.0 | 2391.2 | -2350.2 | 5.8mH | 2468.0 | 2397.0 |
| Top M112 Reservoir |  |  |  |  | 2480.0 | 2408.0 |
| Top M131A Reservoir |  |  |  |  | 2482.0 | 2410.0 |
| Top M131AB Reservoir |  |  |  |  | 2486.0 | 2414.0 |
| Top M132 |  |  |  |  | 2492.0 | 2420.0 |
| Top M141 |  |  |  |  | 2497.0 | 2425.0 |
| Original Oil Water Contact |  |  |  |  | 2512.0 | 2438.0 |
| Total Depth |  |  |  |  | 2552.0 | 2478.2 |

| Current Formation | Lakes Entrance |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 1099.0 | 201.0 | 3.638 | 0.009 | 0.003 | 0.001 | 0.000 | 0 |
| MAX (GFF) | 1201.0 | 125.0 | 2.987 | 0.006 | 0.001 | 0.000 | 0.000 | 0 |
| BG (Reserval) | 1008 - 2329 | 40.5 | 0.718 | 0.003 | 0.001 | 0.001 | 0.000 | - |
| BG (GFF) | 1008 - 2329 | 20.8 | 0.505 | 0.002 | 0.000 | 0.001 | 0.000 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | 1201.0m 1230.0m 1260.0m | 196.3 153.5 122.0 | 3.460 2.864 1.738 | 0.010 0.007 0.005 | 0.002 0.002 0.001 | 0.000 0.000 0.000 | 0.000 0.000 0.000 | 0 0 0 |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3RR |
| SIZE (in) | 9.875 | 14.75 |
| MANUFACTURER/TYPE | Reed Hycalog, RSX616M | Reed Hycalog, P11 |
| JETS (/32 inch) | 3 x 14 / 3 x 16 | 2 x 24 |
| DEPTH IN (m) | 589.62 | 202.5 |
| DEPTH OUT (m) | - | 589.62 |
| METRES ON RUN (m) | - | 387 |
| HRS ON BTM 24hrs/total | 15.8 / 22.6 | 0 / 12.1 |
| BIT CONDITION | - | 1-1-WT-A-E-IN-NO-TD |
| RPM RANGE 24hrs | 101 -169 | - |
| Pump Hrs 24 hrs / total | 20.0 / 33.8 | 0 / 24.5 |
| Krevs 24 hrs / total | 126.8 / 174.5 | 0 / 40.9 |

| 24 HOUR SUMMARY | Drill and survey 9-7/8” hole from 1008.0 mMDRT to 2370.0 mMDRT as per Anadrill’s instructions. |
| --- | --- |
| 24-06-2009 5 AM UPDATE | Wash & ream OOH one stand while circulating 1x bottom’s up at 700gpm with 3275psi. Drill 9-7/8" production hole with RSS Powerdrive assembly from 2370m to 2494m. AM DEPTH: 2494.0 mMDRT (2420.5 mTVDRT) |