Report for : Mark Callictt / Sam Falkener

Compiled by : Gareth Munro

| WELL | CBA F27 |
| --- | --- |
| DATE | 21-05-2009 |
| REPORT # | 15 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole to TD. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2276.0 mMDRT |  | MINIMUM | 11.52 | 1668.0 |
| TVD | 1591.0 mTVDRT |  | MAXIMUM | 102.21 | 2041.0 |
| PROGRESS LAST 24 hrs | 845 |  | AVERAGE | 57.48 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 3449.6 | 2185.0 |
| Top of Latrobe Group |  |  |  |  | 3773.9 | 2352.0 |
| Top Coarse Clastics |  |  |  |  | 3777.8 | 2354.0 |
| Top M101B Upper Reservoir |  |  |  |  | 3779.7 | 2355.0 |
| Top M101D Upper Reservoir |  |  |  |  | 3787.5 | 2359.0 |
| Top M101D Lower Reservoir |  |  |  |  | 3797.2 | 2364.0 |
| Top M101E Reservoir |  |  |  |  | 3814.7 | 2373.0 |
| M111 Reservoir |  |  |  |  | 3838.0 | 2385.0 |
| M131 Reservoir |  |  |  |  | 3898.2 | 2416.0 |
| Original Oil Water Contact |  |  |  |  | 3942.8 | 2439.0 |
| Total Depth |  |  |  |  | 3982.8 | 2459.6 |

| Current Formation | LIMESTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 1683.0 | 45.0 | 0.792 | 0.002 | 0.001 | 0.001 | 0.001 | 0 |
| MAX (GFF) | 1808.0 | 38.0 | 0.780 | 0.003 | 0.000 | 0.001 | 0.001 | 0 |
| BG (Reserval) | - | 24.4 | 0.429 | 0.001 | 0.001 | 0.001 | 0.000 | - |
| BG (GFF) | - | 24.5 | 0.460 | 0.003 | 0.000 | 0.001 | 0.000 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 7 | 6 |
| SIZE (in) | 9-7/8 | 9-7/8 |
| MANUFACTURER/TYPE | Reed Hycalog / RSD616M | Mill Tooth |
| JETS (/32 inch) | 6 x 18 | 3 x 22 |
| DEPTH IN (m) | 603 | 599 |
| DEPTH OUT (m) | - | 603 |
| METRES ON RUN (m) | - | 4 |
| HRS ON BTM 24hrs/total | 14.7 / 38.4 | 0.0 / 0.6 |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 141 - 181 | - |
| Pump Hrs 24 hrs / total | 20.5 / 54.6 | 0 / 14.2 |
| Krevs 24 hrs / total | 131/ 330 | 0 / 2 |

| 24 HOUR SUMMARY | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions. |
| --- | --- |
| 22-05-2009 5AM UPDATE | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions. 5AM DEPTH: 2451.0 mMDRT |