Report for : Mark Calicutt / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA F27 |
| --- | --- |
| DATE | 24-05-2009 |
| REPORT # | 18 |
| MIDNIGHT ACTIVITY | Back reaming out of hole at 3355.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3983.0 mMDRT |  | MINIMUM | 15.7 | 3879.0 |
| TVD | 2465.6 mTVDRT |  | MAXIMUM | 66.4 | 3765.0 |
| PROGRESS LAST 24 hrs | 307.0 m |  | AVERAGE | 34.9 | 3676.0-3983.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3436.0 | 2184.7 | -2143.7 | 0.3 H | 3449.6 | 2185.0 |
| Top of Latrobe Group | 3769.5 | 2356.4 | -2315.4 | 4.4 L | 3773.9 | 2352.0 |
| Top Coarse Clastics | 3772.5 | 2357.9 | -2316.9 | 3.9 L | 3777.8 | 2354.0 |
| Top M101B Upper Reservoir | 3781.5 | 2362.5 | -2321.5 | 7.5 L | 3779.7 | 2355.0 |
| Top M101D Upper Reservoir | 3785.5 | 2364.5 | -2323.5 | 5.5 L | 3787.5 | 2359.0 |
| Top M101D Lower Reservoir | 3797.0 | 2370.4 | -2329.4 | 6.4 L | 3797.2 | 2364.0 |
| Top M101E Reservoir | 3811.0 | 2377.6 | -2336.6 | 4.6 L | 3814.7 | 2373.0 |
| M111 Reservoir | 3828.0 | 2386.3 | -2345.3 | 1.3 L | 3838.0 | 2385.0 |
| M131 Reservoir | 3887.0 | 2416.5 | -2375.5 | 0.5 L | 3898.2 | 2416.0 |
| Total Depth | 3983.0 | 2465.7 | -2424.7 | 6.1 L | 3982.8 | 2459.6 |

| Current Formation | SANDSTONE, SILTSTONE, COAL. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3787.0 | 75.1 | 0.482 | 0.125 | 0.152 | 0.103 | 0.034 | 0 |
| MAX (GFF) | 3808.0 | 86.8 | 0.468 | 0.146 | 0.182 | 0.145 | 0.058 | 0 |
| BG (Reserval) | 3676.0-3983.0 | 19 | 0.122 | 0.026 | 0.031 | 0.023 | 0.008 | - |
| BG (GFF) | 3676.0-3983.0 | 29 | 0.171 | 0.040 | 0.042 | 0.018 | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 7 | 6 |
| SIZE (in) | 9-7/8 | 9-7/8 |
| MANUFACTURER/TYPE | Reed Hycalog / RSD616M | Mill Tooth |
| JETS (/32 inch) | 6 x 18 | 3 x 22 |
| DEPTH IN (m) | 603.0 | 599 |
| DEPTH OUT (m) | - | 603 |
| METRES ON RUN (m) | 3380.0 | 4 |
| HRS ON BTM 24hrs/total | 8.8 / 69.2 | 0.0 / 0.6 |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 90-160 | - |
| Pump Hrs 24 hrs / total | 19.4 / 115.9 | 0 / 14.2 |
| Krevs 24 hrs / total | 53 / 575 | 0 / 2 |

| 24 HOUR SUMMARY | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3676.0 mMDRT to 3983.0 mMDRT, taking SCR’S at 3850.0 mMDRT. Circulate and work pipe from 3983.0 mMDRT to 3966.0 mMDRT, Anadrill downlink to tools and take surveys. Back ream out of hole from 3983.0 mMDRT to 3909.0 mMDRT, racking back a stand every bottoms up. Back ream out of hole at 10 minutes a stand from 3909.0 mMDRT to 3355.0 mMDRT. |
| --- | --- |
| 25-05-2009 5AM UPDATE | Back ream out of hole at 10 minutes a stand from 3355.0 mMDRT to 2815.0 mMDRT. 5AM DEPTH: 3983.0 mMDRT (2465.6 mTVDRT) |