Report for : Mark Calicut / Andy Choy

Compiled by : Colin Chadwick

| WELL | CBA F8A |
| --- | --- |
| DATE | 06-06-2009 |
| REPORT # | 05 |
| MIDNIGHT ACTIVITY | Drilling ahead 9-7/8” hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2776.0 mMDRT |  | MINIMUM | 26.12 | 2047.0 |
| TVD | 2194.0 mTVDRT |  | MAXIMUM | 120.49 | 2543.0 |
| PROGRESS LAST 24 hrs | 965.0 m |  | AVERAGE | 74.23 | 1811.0-2776.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 2715.0 | 2145.0 | -2105.0 | 32.0 H | 2753.0 | 2178.0 |
| Top of Latrobe Group |  |  |  |  | 3048.8 | 2404.0 |
| Top Coarse Clastics |  |  |  |  | 3051.4 | 2406.0 |
| Top M101D Reservoir |  |  |  |  | 3052.7 | 2407.0 |
| Top M101E Reservoir |  |  |  |  | 3060.0 | 2412.0 |
| Top M111 Reservoir |  |  |  |  | 3065.3 | 2417.0 |
| Total Depth |  |  |  |  | 3133.1 | 2468.6 |

| Current Formation | Gippsland Limestone |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 1834.0 | 59.0 | 1.092 | 0.002 | 0.001 | 0.001 | 0.000 | - |
| MAX (GFF) | 1875.0 | 65.0 | 1.111 | 0.003 | 0.000 | 0.000 | 0.000 | - |
| BG (Reserval) | 1811.0-2776.0 | 24.4 | 0.461 | 0.001 | 0.000 | 0.001 | 0.000 | - |
| BG (GFF) | 1811.0-2776.0 | 21.3 | 0.357 | 0.001 | 0.000 | 0.000 | 0.000 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9⅞ |  |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 |  |
| JETS (/32 inch) | 6 x 18 |  |
| DEPTH IN (m) | 696.0 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | 2080.0 |  |
| HRS ON BTM 24hrs/total | 13 / 42.6 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 95-142 |  |
| Pump Hrs 24 hrs / total | 21 / 70 |  |
| Krevs 24 hrs / total | 101 / 285 |  |

| 24 HOUR SUMMARY | Drill 9-7/8” hole from 1811.0 mMDRT to 2776.0 mMDRT. |
| --- | --- |
| 07-06-2009 5AM UPDATE | Drill 9-7/8” hole from 2776.0 mMDRT to 2979.0 mMDRT. 5AM DEPTH: 2979.0 mMDRT (2349.8 mTVDRT) |