Report for : Mark Calicut / Andy Choy / Dan Daniels

Compiled by : Colin Chadwick

| WELL | CBA F8A |
| --- | --- |
| DATE | 07-06-2009 |
| REPORT # | 06 |
| MIDNIGHT ACTIVITY | Back-reaming OOH @ 2044.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3137.0 mMDRT |  | MINIMUM | 19.19 | 2964.5 |
| TVD | 2471.0 mTVDRT |  | MAXIMUM | 98.16 | 2980.5 |
| PROGRESS LAST 24 hrs | 361.0 m |  | AVERAGE | 52.32 | 2776.0-3137.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 2715.0 | 2146.0 | -2105.0 | -32.0 H | 2753.0 | 2178.0 |
| Top of Latrobe Group | 3054.5 | 2406.0 | -2365.0 | 2.0 L | 3048.8 | 2404.0 |
| Top Coarse Clastics | 3057.0 | 2407.9 | -2366.9 | 1.9 L | 3051.4 | 2406.0 |
| Top M101D Reservoir | 3059.1 | 2409.5 | -2368.5 | 2.5 L | 3052.7 | 2407.0 |
| Top M101E Reservoir | 3062.5 | 2412.1 | -2371.1 | 0.1 L | 3060.0 | 2412.0 |
| Top M111 Reservoir | 3068.9 | 2417.0 | -2376.0 | 0.0 | 3065.3 | 2417.0 |
| HOOWC | 3096.3 | 2438.0 | -2397.0 | 0.0 | 3093.3 | 2438.0 |
| Total Depth | 3137.0 | 2469.0 | -2427.95 | -0.1 H | 3133.1 | 2468.6 |

| Current Formation | LATROBE GROUP |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3108.0 | 69.0 | 0.504 | 0.086 | 0.119 | 0.094 | 0.033 | - |
| MAX (GFF) | 3106.5 | 56.0 | 0.205 | 0.063 | 0.107 | 0.103 | 0.043 | - |
| BG (Reserval) | 2776.0-3137.0 | 10.9 | 0.121 | 0.008 | 0.011 | 0.010 | 0.003 | - |
| BG (GFF) | 2776.0-3137.0 | 12.6 | 0.139 | 0.007 | 0.009 | 0.008 | 0.001 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9⅞ |  |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 |  |
| JETS (/32 inch) | 6 x 18 |  |
| DEPTH IN (m) | 696.0 |  |
| DEPTH OUT (m) | 3137.0 |  |
| METRES ON RUN (m) | 2441 |  |
| HRS ON BTM 24hrs/total | 6.9 / 49.5 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 80-142 |  |
| Pump Hrs 24 hrs / total | 19 / 89 |  |
| Krevs 24 hrs / total | 46 / 331 |  |

| 24 HOUR SUMMARY | Drill 9-7/8” hole from 2776.0 mMDRT to 3137.0 mMDRT. Circulate 3 x bottoms up racking back one stand per circulation to 3066.0 mMDRT. Backream out of hole with 750 gpm from 3066.0 mMDRT to 2044.0 mMDRT |
| --- | --- |
| 08-06-2009 5AM UPDATE | Backream out of hole with 750 gpm from 2044.0 mMDRT to 1373.0 mMDRT. 5AM DEPTH: 3137.0 mMDRT (2468.95 mTVDRT) |