@

| Date: | 8 January 2009 | Licence / State: | VIC/P46 |
| --- | --- | --- | --- |
| Report Period: | 06:00 – 06:00 hrs AEDT | Rig: | Seadrill: West Triton |
| Days From Spud: | 25 | RT - SEAFLOOR: | 76.7m |
| Current Hole Size: | 216mm (8.5”) | WATER DEPTH | 38.7 m MSL |
|  |  | RT: | 38.0 m MSL |
| Depth @ 06:00 Hrs EST: | 3585m MDRT | PTD: | 4000.0 m MDRT |
|  | 3580.4m TVDRT | Spud Date: | 14 December 2008 |
|  | -3542.4 SS |  |  |
| 24 Hr Progress: 06:00 – 06:00 EST | 0m |  |  |
| Current Operation: | POH Run 1 E-Logs PEX-RES-SON |
| AFE Cost (Drill)$ | (Coal&S)$ |  | Cost To Date: |
|  | (P&A)$ |  |  |

| Casing Data | Hole Size | Depth | Casing Size | Wt: | Type | Shoe Depth | LOT/FIT |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 914 mm (36”) | 119m | 762mm (30”) |  | X52 | 116m |  |
| 2 | 444mm (17.5”) | 999m | 340mm(13.375”) | 68lb/ft | NT80HE | 987m | - / 15.0ppg EMW |
| 3 | 311mm(12.25”) | 2807 | 244mm(9.675”) | 53.5lb/ft | P110 | 2800.3m | - / 16.0ppg EMW |

| Mud Data | Type: | Wt: | Visc: | WL: | PH: | KCl: | Cl -: | PV/YP: | Rmf |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10.00 | KCl Polymer | 11 | 50 | 6 | 8.5 | 7% | 40k | 23/28 | - |

| Bit Data | No. | Make | Type | Size | Hours | Meters | Condition |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Present | 6 | Security | PDC | SE3653Z | 216mm (8.5”) | 42.4 | 778 | 1 1 CT N X I NO TD |
| Last | 5 | Reed | PDC | RSX616M-A10 | 311mm (12.25”) | 19.3 | 410.5 | 1 1 LT G X I BU TD |

| Surveys | Type | MD (m) | Inclination | Azimuth (T) | TVD (m) | Offset (m) | Direction (T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 103 | MWD | 3569.38 | 7.28 | 160.29 | 3564.07 | 91.88 | 191.43 |

| Fluid Loss | Interval MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |

OPERATIONS SUMMARY

Previous 24 hrs Operations Summary at 06:00 hrs AEDT

Washed and reamed 3576-3585m – hole packing off below 3576m.  Circulated hole clean and raised mud weight to 11.0ppg.  POH.  Downloaded Radio Active sources.  Laid out LWD tools.  Rigged up wireline loggers.  RIH Run 1 PEX-RES-SON.  Logged up Run 1 end log at casing shoe.  POH Run 1.

Anticipated operations:

Continue E-Logs. Run 2 MDT-GR.

| FORMATION TOPS |
| --- |
| FORMATION | ACTUAL TOP | High / Low | High / Low | PROGNOSED TOP |
|  | (MDmRT) | (mSS) | Prognosis | Normanby-1 | (MDmRT) | (mSS) |
| Heytesbury Group | 76.7 | -38.7 | 0m | 10 High | 76.7 | -38.7 |
| Nirranda Group | 492 | -454 | 49m Low | 145 High | 443.0 | -405.0 |
| Dilwyn Formation | 576 | -538 | 38m Low | 152 High | 538.0 | -500.0 |
| Pember Mudstone | 963 | -925 | 15m Low | 255 High | 948.0 | -910.0 |
| Pebble Point Formation | 1075 | -1037 | 47m Low | 227 High | 1028.0 | -990.0 |
| Timboon Sandstone | 1092 | -1054 | 44m Low | 236 High | 1048.0 | -1010.0 |
| Paarratte Formation | 1245 | -1207 | 22m Low | 251 High | 1223.0 | -1185.0 |
| Skull Creek Mudstone | 1705 | -1666 | 1m Low | 258 High | 1703.0 | -1665.0 |
| Nullawarre Greensand | 1850 | -1811 | 26m Low | 232 High | 1823.0 | -1785.0 |
| Belfast C & B Mudstone | 1905 | -1866 | 26m Low | 232 High | 1878.0 | -1840.0 |
| Belfast A Mudstone | 2160 | -2120 | 5m High | 253 High | 2163.0 | -2125.0 |
| Flaxman Formation | 2873 | -2832 | 68m High | 363m Low | 2938.0 | -2900.0 |
| Waarre Formation Unit C | 3186 | -3145 | 45m High | 385m Low | 3228.0 | -3190.0 |
| Waarre Formation Unit B |  |  |  |  | 3533.0 | -3495.0 |
| Waarre Formation Unit A |  |  |  |  | 3588.0 | -3550.0 |
| Eumeralla Formation |  |  |  |  | 3988.0 | -3950.0 |
| Total Depth |  |  |  |  | 4000.0 | -3962.0 |

HYDROCARBON SHOW SUMMARY

| INTERVAL | LITHOLOGY & HYDROCARBON FLUORESCENCE | GAS |
| --- | --- | --- |
| 3585m | No new formation drilled |  |

| GAS | MD (m) | Peak | Background | Chromatograph |
| --- | --- | --- | --- | --- |
| Trip Gas |  |  |  |  |
| Connection Gas |  |  |  |  |

GEOLOGICAL SUMMARY

| INTERVAL ROP (m/hr) | LITHOLOGY | GAS (Peak / BG) Composition % |
| --- | --- | --- |
| 3585 | No new formation drilled |  |

REMARKS:

DGR 26 links to DDR 29.

Hole good while logging out on wireline.  Line tension overpulls due to line drag – head tension normal.

LWD Offsets from Bit:

Run 4:

Memory data downloaded.  Sonic data with processing centre.

Geologists:  Greg Clota/BrianRicketts