WEEKLY REPORT

Week Ending		12 July 2009

________________________________________________________________________________

Well			GV Cotswold 1

Location		As Drilled

754657 m E	5884058 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		320.1 metres	target depth

Well Details		0 – 21.0 m		Open Hole 	170mm

21.0 – 101.9 m	PQ Core

101.9 – 320.1 m	HQ Core

Casing			0 – 5.0 m 	PVC	150mm

0 – 102.0 m	HW	cemented

0 – 320.1 m	63mm 	Poly pipe casing

________________________________________________________________________________

Well			GV Werona 1

Location		37.25 deg S	144.03 deg N

237005 m E	5872719 m N	Zone 55	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		219.0 metres

Well Details		0 – 10.9 m		Open Hole 	170mm

10.9 – 63.4 m		PQ Core

63.4 – 219.0 m	HQ Core

Casing			0 – 6.0 m 	PVC	150mm

0 -63.4 m	HW	cemented

________________________________________________________________________________

Well			GV Carisbrook 1

Location		37.04 deg S	143.88 deg N

755799 m E	5897341 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		95.9 metres

Well Details		0 – 14.0 m		Open Hole 	170mm

14.0 – 95.9 m		PQ Core

Casing			0 – 3.0 m 	PVC	150mm	casing retrieved

Other	Well collapsed when attempting to run HW casing. Unable to run HW casing. Well abandoned

________________________________________________________________________________

Well			GV Carisbrook 2

Location		37.04 deg S	143.88 deg N

755799 m E	5897341 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		34.0 metres

Well Details		0 – 11.1 m		Open Hole 	170mm

11.1 – 34.0 m		PQ Core

Casing			0 – 7.0 m 	PVC	150mm

Other	Well proceeding satisfactorily.

________________________________________________________________________________

Safety	Heavy rain in area during the week making paddock access and paddock areas very soft. Paddock traffic being minimised.

Environment	No issues to report

Landholder Issues

No issues

Other	GV Cotswold 1 completed on 6 July 2009

GV Carisbrook 1 commenced drilling 8 July 2009

GV Carisbrook 1 abandoned drilling 10 July 2009

Well collapsed and it was not possible to run any HW casing.

Rig moved approximately ten metres

GV Carisbrook 2 commenced drilling 11 July 2009

Rob Murphy

Geogen Victoria

Ballarat Operations