WEEKLY REPORT

Week Ending		13 September 2009

_______________________________________________________________________________

Well			GV Cameron 2

Location		As drilled

748903 m E	5878549 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		320.0 metres		Target Depth

Well Details		0 – 6.6 m		Open Hole 	170mm

6.6 – 52.2 m		PQ Core

52.2 – 92.1 m		Open Hole	PCD

92.1 – 123.0 m	PQ Core

123.0 – 320.0 m	HQ Core

Casing			0 – 6.6 m 	PVC	150mm

0 – 123 m	HW 	cemented

0 – 300 m	Poly casing	63mm

Other	No issues

________________________________________________________________________________

Well			GV Leishman 2

Location		As being drilled

753312 m E	5873009 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		171.8 metres

Well Details		0 – 4.0 m		Open Hole 	170mm

4.0 – 85.3 m		PQ Core

85.3 – 130.2 m	Open Hole	PCD

130.2 – 135.1 m	HQ Core	no core recovered

135.1 – 147.0 m	Open hole	PCD

147.0 – 171.8 m	HQ Core

Casing			0 – 4.0 m 	PVC	150mm

0 – 147.0 m	HW

Other	Drilling conditions in Calivil Formation sands to 147 metres difficult.

________________________________________________________________________________

Safety	No incidents to report.

Environment	GV Leishman 2, minor diesel spill (<2 litres), when hose from 200 litre drum pump leaked diesel onto light vehicle tray and subsequently onto ground. Spill kit materials available and used and small amount of contaminated soil removed from site

Landholder Issues

No issues to report

Other		GV Cameron 2 commenced drilling 28 August 2009

GV Cameron 2 completed drilling on 6 September 2009

Poly casing to be run in well on 7 September 2009

GV Leishman 2 is commenced drilling on 9 September 2009

GV Pastoria 1 will follow the completion of GV Leishman 2

Rob Murphy

Geogen Victoria

Ballarat Operations