WEEKLY REPORT

Week Ending		16 August 2009

_______________________________________________________________________________

Well			GV Cameron 1

Location		37.20 deg. S	143.80 deg. N

748911 m E	5878577 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		206.7 metres

Well Details		0 – 5.0 m		Open Hole 	170mm

5.0 – 122.9 m		PQ Core

122.9 – 206.7 m	HQ Core

Casing			0 – 2.0 m 	PVC	150mm

0 – 122.9 m	HW	cemented

Other	No issues

________________________________________________________________________________

Well			GV Goldsmith 1

Location		39.55 deg. S	143.35 deg.E

707874 m E	5841116 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		240.1 metres

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 113.6 m		PQ Core

113.6 – 240.1 m	HQ Core

Casing			0 – 4.5 m 	PVC	150mm

0 – 113.6 m	HW 	cemented

Other	No issues

________________________________________________________________________________

Safety	No incidents to report.

Environment	Site refurbishment of GV Moolort 1-3, GV Addington 1 and GV Stewart 1 completed.

Oil leaks reported on Rig 6 at GV Goldsmith 1. Oil being contained with spill kit materials.

Landholder Issues

No issues to report

Other		GV Goldsmith 1 commenced drilling 4 August 2009

GV Cameron 1 commenced drilling 10 August 2009

GV Leishman is expected to commence 18 August 2009

GV Addington 1. Following five shifts with poor progress and increasing well instability, a night shift was worked on 1 August 2009 (276.3 – 295m) in an effort to try to achieve a well depth close to the target depth of 320 metres. The well was stopped on 2 August at 298.8 metres. A night shift at GV Stewart 1 was lost, as the night shift crew worked at GV Addington 1.

Vic DPI officers visited GV Cameron 1, GV Goldsmith 1, and the sites of GV Moolort 1 – 3 and GV Leishman 1. As a result of the visit further information has been requested.

Rig 13 will stood down at the completion of GV Cameron 1

Rob Murphy

Geogen Victoria

Ballarat Operations