WEEKLY REPORT

Week Ending		19 July 2009

________________________________________________________________________________

Well			GV Werona 1

Location		As drilled

237008 m E	5872713 m N	Zone 55	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		319.1 metres	Target depth

Well Details		0 – 10.9 m		Open Hole 	170mm

10.9 – 63.4 m		PQ Core

63.4 – 319.1 m	HQ Core

Casing			0 – 6.0 m 	PVC	150mm

0 -63.4 m	HW	cemented

0 – 319.1 m	63mm	Poly pipe

________________________________________________________________________________

Well			GV Carisbrook 1

Location		As drilled

755798 m E	5897329 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		95.9 metres

Well Details		0 – 14.0 m		Open Hole 	170mm

14.0 – 95.9 m		PQ Core

Casing			0 – 3.0 m 	PVC	150mm	casing retrieved

Other	Well collapsed when attempting to run HW casing. Unable to run HW casing. Well abandoned

________________________________________________________________________________

Well			GV Carisbrook 2

Location		As drilled

755795 m E	5897327 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		320.0 metres	Target depth

Well Details		0 – 11.1 m		Open Hole 	170mm

11.1 – 105.0 m	PQ Core

105.0 – 320.0 m	HQ core

Casing			0 – 7.0 m 	PVC	150mm

0 – 105.0 m	HW	cemented

0 – 320.0 m	63mm	Poly pipe

Other	Access to paddock poor

________________________________________________________________________________

Well			GV Addington 1

Location		37.41 deg. S	143.66 deg. E	(approx.)

735904 m E	5855956 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		36.6 metres

Well Details		0 – 4.8 m		Open Hole 	170mm

4.8 -36.6 m		PQ Core

Casing			0 – 4.8 m 	PVC	150mm

Other	Access to paddock poor

________________________________________________________________________________

Safety	Paddock traffic being minimised.

Environment	No issues to report

Landholder Issues

No issues

Other	GV Carisbrook 2 completed drilling 19 July 2009

GV Werona 1 completed drilling 15 July 2009

GV Addington 1 commenced drilling 18 July 2009

GV Moolort 1 expected to commence drilling 20 July 2009

Rob Murphy

Geogen Victoria

Ballarat Operations