WEEKLY REPORT

Week Ending		23 August 2009

_______________________________________________________________________________

Well			GV Cameron 1

Location		As drilled

748906 m E	5878549 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		320.0 metres	Target depth

Well Details		0 – 5.0 m		Open Hole 	170mm

5.0 – 122.9 m		PQ Core

122.9 – 320.0 m	HQ Core

Casing			0 – 2.0 m 	PVC	150mm

0 – 122.9 m	HW	cemented

0 – 320.0 m	Poly	63mm

Other	HQ rod string dropped when making final extraction from hole after running poly inside HQ rod string. Incident being investigated. Rods recovered. Poly casing recovery in progress. A new poly casing string will be run when original poly casing string recovered.

________________________________________________________________________________

Well			GV Goldsmith 1

Location		As drilled

707872 m E	5841112 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		315.5 metres	Target depth

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 113.6 m		PQ Core

113.6 – 315.5 m	HQ Core

Casing			0 – 4.5 m 	PVC	150mm

0 – 113.6 m	HW 	cemented

0 – 315.5 m	Poly	63mm

Other	No issues

________________________________________________________________________________

Safety	No incidents to report.

Environment	No issues to report

Landholder Issues

No issues to report

Other		GV Goldsmith 1 completed drilling 19 August 2009

GV Cameron 1 completed drilling 18 August 2009

GV Leishman 2 commencement has been delayed, whilst GV Cameron 1 is recovered

Rob Murphy

Geogen Victoria

Ballarat Operations