| Date: | 25 Oct 2009 | Report Number: | 9 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 1558 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 1284 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 274 m | FIT: | 1.7 sg |
| Lag Depth: | 1528 | Mud Weight: | 1.26 sg |
| Water Depth: | 503.0 m LAT | ECD: | 1.33 sg EMW |
| RT: | 21.5 m | Mud Type: | Ultradrill |
| Last Survey Depth: | 1450.69 mMDRT | Mud Chlorides: | 65,000 |
| Deviation: | Inc 0.32° Azi 100.66° | Est. Pore Press: | 1.10 sg EMW |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Continued RIH, tagged top of cement at 1244.87 mMDRT. Drilled out cement float and shoe track whilst displacing to new Ultradrill mud system. Drilled 5 m of new formation. Conducted LOT to 1.7 sg EMW (824psi) with 1.25 sg mud. Performed SCRs. Conducted rig shut down safety talk. Drilled 311 mm (12-1/4”) hole from 1284 to 1558 mMDRT. |
| --- | --- |
| NEXT 24 HOURS: | Drill 311 mm (12-1/4”) hole. |
| MIDNIGHT TO 0600hrs SUMMARY: | Drilled 311 mm (12.25”) hole from 1558 to 1715 mMDRT whilst increasing mud weight to 1.3 sg. |
| CURRENT OPERATION @ 06:00hrs: | Drilling 311 mm (12.25”) hole at 1715 mMDRT |

## GEOLOGICAL SUMMARY

LITHOLOGY

INTERVAL:	1284 to 1440 mMDRT

ROP (range):	5.2 to 196.6 m/hr

ROP (av):	50.0 m/hr

CALCAREOUS CLAYSTONE finely interbedded and gradational with ARGILLACEOUS CALCISILTITE

CALCAREOUS CLAYSTONE (40 to 90%):  light olive grey to greenish grey, firm, sub-blocky to blocky, 20 to 40% calcareous, trace to 1% calcareous silt, trace dark silt, in part trace blocky pyrite, in part trace very fine quartz sand, in part trace yellow calcareous grains, in part trace glauconite, in part trace reddish brown lithics, in part trace skeletal fragments, grades in part to Argillaceous Calcisiltite.

ARGILLACEOUS CALCISILTITE (10 to 60%):  patchy white, very light patchy grey to very light olive grey, firm to in part moderately hard, sub-blocky to blocky, 20 to 30% argillaceous, trace dark silt and flecks, trace calcite crystals and grains, in part trace to 1% quartz silt and sand, trace to 1% very fine black glauconite grains.

INTERVAL:	1440 to 1520 mMDRT

ROP (range):	23.8 to 160.0 m/hr

ROP (av):	53.3 m/hr

Interbedded CALCAREOUS CLAYSTONE and ARGILLACEOUS CALCISILTITE

CALCAREOUS CLAYSTONE (70 to 90%):  light olive grey  to olive grey, greenish grey to dark greenish grey, soft to firm, sub-blocky to blocky, 30 to 40% calcareous clay, trace to 1% calcareous silt, trace carbonaceous specks, trace glauconite silt, trace pyrite.

ARGILLACEOUS CALCISILTITE (10 to 30%):  light olive grey to light grey, trace white patches, firm, sub-blocky to blocky, 25% argillaceous, trace calcite crystals, trace very fine lithics, gradational Argillaceous Calcilutite in part.

HYDROCARBON FLUORESCENCE

# No hydrocarbon fluorescence.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1284-1440 | 0.0132 | 0.0038 | - | - | - | - | - | - |
| 1440-1520 | 0.0333 | 0.0164 | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.26 sg |
| Connection gas | Nil |
| Trip gas | Nil |
| Background gas | Low background gas levels. Slowly increasing trend with depth. |
| Dxc exponent | Minor cutback at 1104 mMDRT. No other cut backs observed. |
| ROP | No signs of over pressure. Normal reflecting changes in formation |
| Ditch cuttings | No splintery or pressure style cavings observed |
| Mud temperature out | No indication of overpressure |
| MWD resistivity | Minor overpressure at 1430, 1460, 1485, 1455 mMDRT (from town Pore Pressure analyst support), but is still less than the pre-drill prediction from town. |
| Pore Pressure Estimate | ~1.1 sg EMW (estimate from town Pore Pressure support based on resistivity data) |

# SAMPLE QUALITY

# Good.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All equipment operating and functional.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: During the first shallow hole test RT communication to the sADN tool failed. The tool was broken out and laid down while checks were done on the sonic tool. After inspection the sonic was found to have a faulty extender. The sonic was laid out. The back-up sonic and sADN tools were picked up.

The 444 mm (17.5”) tools were back loaded on 25th October 2009.

| Sensor | Distance from Bit (m) |
| --- | --- |
| Pressure (Arc) | 9.31 |
| Resistivity(Arc) | 10.03 |
| Gamma Ray (Arc) | 10.08 |
| Vibration (TeleScope) | 17.05 |
| Direction & Inclination (TeleScope) | 18.05 |
| Delta T (sonic) | 27.56 |
| Ultrasonic (sADN) | 33.34 |
| Density (sADN) | 33.51 |
| Neutron (sADN) | 35.49 |

###### WIRELINE

Personnel: No crew onboard.

REMARKS

None

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 | 1330 | 1329.93 | 1308.43 | -1.57 | LWD |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 |  |  |  |  |  |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 |  |  |  |  |  |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 |  |  |  |  |  |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 |  |  |  |  |  |
| Thylacine Member |  | 2832.5 | 2811.0 | 170 |  |  |  |  |  |
| Flaxman Formation |  | 2858.5 | 2837.0 | 180 |  |  |  |  |  |
| Waare Formation |  | 3154.5 | 3133.0 | 220 |  |  |  |  |  |
| Eumeralla Formation |  | 3276.5 | 3255.0 | 240 |  |  |  |  |  |
| TD |  | 3326.0 | 3304.4 | 240 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| 1284-1290 | 6 |  |
| 1290-1520 | 10 |  |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| 1289 | Mud |
| 1289 | Filtrate |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| 1300 | 25 Oct 09 | 17:08 | 0.0065 |  |
| 1400 | 25 Oct 09 | 20:31 | 0.0162 |  |
| 1500 | 25 Oct 09 | 23:18 | 0.0285 |  |