| Date: | 27 Oct 2009 | Report Number: | 11 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 2912 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 2288 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 624 m | FIT: | 1.7 sg |
| Lag Depth: | 2878 mMDRT | Mud Weight: | 1.31 sg |
| Water Depth: | 503.0 m LAT | ECD: | 1.36 sg EMW |
| RT: | 21.5 m | Mud Type: | Ultradrill |
| Last Survey Depth: | 2863.33 mMDRT | Mud Chlorides: | 52,000 |
| Deviation: | Inc 1.15° Azi 160.56° | Est. Pore Press: | 1.38 sg EMW @ ~2655 mMDRT |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Drilled 311 mm (12.25”) vertical hole from 2288 to 2912 mMDRT. Flow checked well and closed in on kick. Weighed up kill mud to 1.5 sg (12.5ppg). Commenced pumping kill mud to bit. |
| --- | --- |
| NEXT 24 HOURS: | Continue to circulate well to kill mud. |
| MIDNIGHT TO 0600hrs SUMMARY: | Pumped 1.5 sg (12.5 ppg) kill mud down drill string. No mud returns while pumping. Rig was unable to follow step down chart with choke closed as DP pressure was constantly below calculated expectations. 25.6m3 (161 barrels) of 12.5ppg kill mud pumped surface to bit. With pumps shut off. SIDPP 40psi, SICP 710psi. Monitored well pressures while Drilling team assessed situation and reviewed remedial options. |
| CURRENT OPERATION @ 06:00hrs: | Well closed in for well control operations. |

## GEOLOGICAL SUMMARY

LITHOLOGY

INTERVAL:	2260 to 2310 mMDRT

ROP (range):	16.6 to 72.6 m/hr

ROP (av):	35.6 m/hr

Massive SILTY CLAYSTONE with trace very thin CALCAREOUS CLAYSTONE stringers

SILTY CLAYSTONE (98 to 100%): dark grey, minor brownish grey to dark olive grey, soft to firm, amorphous to sub-blocky, 20 to 25% silt, trace very fine quartz grains, trace very fine glauconite specks, trace silty lithics.

CALCAREOUS CLAYSTONE (0 to 2%): mottled to patchy appearance, light brownish grey to brownish grey, in part white patches, soft to firm, trace moderately hard, in part brittle, sub-blocky to blocky, 20 to 25% calcareous, trace to 3% calcareous silt, trace calcareous fragments, trace to 5% dolomite cement, trace fossil fragments.

INTERVAL:	2310 to 2450 mMDRT

ROP (range):	16.6 to 77.3 m/hr

ROP (av):	42.2 m/hr

SILTY CLAYSTONE with very thin SANDSTONE interbeds

SILTY CLAYSTONE (85 to 100%): dark grey to olive black, olive grey to brownish grey, soft to firm, amorphous to sub-blocky, 20 to 25% silt, trace very fine quartz grains, trace very fine glauconite specks, trace silty lithics, trace mottled light olive grey moderate to strongly calcareous fragments, trace broken  white fossil fragments.

SANDSTONE (0 to 15%): light grey, transparent to translucent quartz grains, loose, very fine grained, sub angular to rounded, sub elongate to sub spherical, very well to well sorted, argillaceous matrix in part dispersive and washing out, trace-5% silt, 5% black lithic specks, trace glauconite, trace pyrite, poor to in parts fair inferred porosity, no hydrocarbon fluorescence.

INTERVAL:	2450 to 2610 mMDRT

ROP (range):	22.5 to 74.8 m/hr

ROP (av):	41.7 m/hr

Massive SILTY CLAYSTONE

SILTY CLAYSTONE (100%): dark grey to greyish black, dark grey to olive black, olive grey to brownish grey, soft to firm, amorphous to sub-blocky, 20 to 25% silt, trace very fine quartz grains, trace very fine glauconite specks, trace silty lithics, trace mottled light olive grey fragments, trace broken white calcareous fossil fragments.

INTERVAL:	2610 to 2670 mMDRT

ROP (range):	22.4 to 60.5 m/hr

ROP (av):	39.5 m/hr

Massive SILTY CLAYSTONE

SILTY CLAYSTONE (100%): dark olive grey to brownish grey, soft to firm, amorphous to sub-blocky, 20 to 25% silt, trace to 2% mottled light olive grey moderate to strongly calcareous claystone, trace to 1% very fine quartz grains, trace to 1% silt to very fine glauconite grains, trace very fine lithics.

INTERVAL:	2670 to 2760 mMDRT

ROP (range):	11.4 to 93.6 m/hr

ROP (av):	44.0 m/hr

Massive SILTY CLAYSTONE

SILTY CLAYSTONE: olive grey to brownish grey, soft, amorphous to sub-blocky, 20% silt, trace to 2% mottled light olive grey and moderate to strongly calcareous claystone (trace to 5% dolomite cement in part), trace very fine quartz grains, trace silt to very fine glauconite grains, trace dark specks.

INTERVAL:	2760 to 2817 mMDRT

ROP (range):	19.5 to 94.3 m/hr

ROP (av):	31.5 m/hr

SILTY CLAYSTONE with thin CLAYSTONE interbeds

SILTY CLAYSTONE (80 to 95%): olive grey to brownish grey, soft to firm, amorphous to sub-blocky, 20% silt, trace silt to very fine glauconite grains, trace dark specks (?coal/?lithics)

CLAYSTONE (5 to 20%): mottled light brownish grey to olive grey, firm to in part hard, in part brittle, sub-blocky to sub-fissile, 2 to 5% calcareous, 2 to 5% dolomite cement, trace white calcareous fragments(?fossil debris), trace streaks or laminations.

INTERVAL:	2817 to 2855 mMDRT

ROP (range):	8.2 to 61.5 m/hr

ROP (av):	30.7 m/hr

ARGILLACEOUS SANDSTONE interbedded with SILTY CLAYSTONE and minor CLAYSTONE

ARGILLACEOUS SANDSTONE (10 to 80%): white, clear to translucent quartz sand, predominantly loose disaggregated sand, soft to weakly friable aggregates, lower very fine to fine grained, well sorted, sub-angular to rounded, sub-spherical, 30 to 50% white clay matrix in aggregates (similar appearance to rockflour), weakly calcareous (see note below), trace black silt, poor visible porosity, poor inferred, no shows.

SILTY CLAYSTONE (10 to 80%): olive grey to brownish grey, soft to firm, amorphous to sub-blocky, 20% silt, trace silt to very fine glauconite grains, trace dark specks (?coal/?lithics) (largely clearing from above).

CLAYSTONE (Nil to 20%): mottled light brownish grey to olive grey, firm to in part hard, in part brittle, sub-blocky to sub-fissile, trace to 5% calcareous, 2 to 5% dolomite cement, trace to 1% white calcareous fragments(?fossil debris), trace streaks or laminations

(Note: CaCO3 being added to active mud system).

INTERVAL:	2855 to 2878 mMDRT

ROP (range):	10.3 to 68.3 m/hr

ROP (av):	33.5 m/hr

SANDSTONE thinly interbedded with SILTY CLAYSTONE

SANDSTONE (10 to 70%): clear to translucent white and grey, trace white friable aggregates, predominantly loose disaggregated sand, very fine to very coarse, predominantly fine to medium, poor to moderately sorted, angular to sub-rounded, sub-spherical, 10% white/grey clay/silt matrix, trace to very fine black silt, in part trace reddish brown lithics, poor visible porosity, fair to good inferred porosity, no hydrocarbon fluorescence. (see note below)

SILTY CLAYSTONE (30 to 90%): medium dark grey to olive grey, soft to firm, amorphous to sub-blocky, 20 to 30% silt, trace silt to very fine glauconite grains, trace dark specks and flecks (?coal/?lithics)

(Note: CaCO3 being added to the active mud system)

HYDROCARBON FLUORESCENCE

# No hydrocarbon fluorescence.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2260 – 2310 | 0.0389 | 0.0253 | 0.0004 | 0 | 0 | 0 | 0 | 0 |
| 2310 – 2450 | 0.1192 | 0.0790 | 0.0015 | 0.0006 | 0.0002 | 0 | 0 | 0 |
| 2450 – 2610 | 0.1426 | 0.0960 | 0.0024 | 0.0011 | 0.0003 | 0.0001 | 0 | 0 |
| 2610 – 2670 | 0.1281 | 0.0875 | 0.0026 | 0.0013 | 0.0003 | 0.0002 | 0 | 0 |
| 2670 – 2760 | 0.1144 | 0.0768 | 0.0026 | 0.0014 | 0.0003 | 0.0002 | 0 | 0 |
| 2760 – 2817 | 0.1150 | 0.0765 | 0.0031 | 0.0018 | 0.0003 | 0.0002 | 0 | 0 |
| 2817 – 2855 | 0.8129 | 0.5702 | 0.0135 | 0.0053 | 0.0005 | 0.0006 | 0.0002 | 0.0001 |
| 2855 – 2878 | 1.6022 | 1.4052 | 0.0324 | 0.0122 | 0.0011 | 0.0015 | 0.0004 | 0.0002 |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| 2843.5 | 1.5318 | 1.0560 | 0.0241 | 0.0089 | 0.0008 | 0.0010 | 0.0002 | 0.0001 |
| 2853.5 | 1.7679 | 1.1663 | 0.0270 | 0.0100 | 0.0009 | 0.0012 | 0.0003 | 0.0001 |
| 2855 | 2.6176 | 1.7572 | 0.0402 | 0.0150 | 0.0013 | 0.0017 | 0.0004 | 0.0002 |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.31 sg |
| Connection gas | Nil |
| Trip gas | Nil |
| Background gas | Slowly increasing trend with depth. Associated with the increase in resistivity generated pore pressure above the static mud weight (from ~2520 to 2730 mMDRT) there was an observed increase in background gas levels from less than 0.1% to 0.11% to 0.19%. |
| Dxc exponent | Minor cutback at 1650 mMDRT. No other cut backs observed. |
| ROP | Normal rates reflecting changes in lithologies. |
| Ditch cuttings | No splintery or pressure style cavings observed. |
| Mud temperature out | No indication of overpressure. |
| MWD resistivity | The resistivity generated pore pressure trends were below or approaching the static mud weight from 2280 to 2470 mMDRT. From 2250 to 2295 and 2500 to 2520 mMDRT the static mud weight and resistivity generated pore pressure trends were approaching balance. Resistivity generated pore pressure trends were just above the static mud weight from 2480 to 2500 mMDRT. From ~2540 to 2730 mMDRT the resistivity generated pore pressure was greater than the static mud weight and was on average calculated to be 1.32 to 1.38 sg. |
| Pore Pressure Estimate | Maximum 1.38 sg EMW at ~2655 mMDRT (resistivity generated pore pressure estimate from town support). From 2745 to 2820 mMDRT the resistivity derived pore pressure estimate was below the static mud weight. |

# SAMPLE QUALITY

# Good.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All equipment operating and functional.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: All equipment functioned during drilling operations,

| Sensor | Distance from Bit (m) |
| --- | --- |
| Pressure (Arc) | 9.31 |
| Resistivity(Arc) | 10.03 |
| Gamma Ray (Arc) | 10.08 |
| Vibration (TeleScope) | 17.05 |
| Direction & Inclination (TeleScope) | 18.05 |
| Delta T (sonic) | 27.56 |
| Ultrasonic (sADN) | 33.34 |
| Density (sADN) | 33.51 |
| Neutron (sADN) | 35.49 |

###### WIRELINE

Personnel: 7 x wireline crew on board.

Equipment: The wireline unit was rigged up all equipment transferred on board. The tools for the “firm” case, VSI-GR and PSWC-GR Wireline runs have been successfully tested.

REMARKS

LWD PDF plots, LWD LAS data and BHI surface logging ascii data was provided to town on the hour for real time pore pressure analysis.

Calcium carbonate was added to the mud system from 280 0mMDRT.

Tracer was added to the mud system at 2400 mMDRT.

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 | 1330 | 1329.93 | 1308.43 | -1.57 | LWD |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 | 1602 | 1601.92 | 1580.42 | -1.58 | LWD / Cuttings |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 | 1680 | 1679.92 | 1658.42 | +21.42 | LWD / Cuttings |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 | 1732 | 1731.92 | 1710.42 | +23.42 | LWD / Cuttings |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 | 2140 | 2139.10 | 2117.60 | +33.60 | LWD |
| Thylacine Member |  | 2854 | 2832.5 | 100 | 2817 | 2816.7 | 2795.2 | -37.3 | GR cut back / cuttings |
| Flaxman Formation |  | 2880 | 2858.5 | 180 |  |  |  |  |  |
| Waare Formation |  | 3139 | 3117.5 | 50 |  |  |  |  |  |
| Eumeralla Formation |  | 3261 | 3239.5 | 70 |  |  |  |  |  |
| TD |  | 3311 | 3289.5 | 70 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| 2260 – 2810 | 10 | None |
| 2810 - 2875 | 5 | None |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| 1289 | Mud |
| 1289 | Filtrate |
| 2427 | Mud (Tracer added) |
| 2427 | Filtrate |
| 2820 | Mud (Reservoir) |
| 2820 | Filtrate (Reservoir) |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| 1300 | 25 Oct 09 | 17:08 | 0.0065 | Scheduled Sample |
| 1400 | 25 Oct 09 | 20:31 | 0.0162 | Scheduled Sample |
| 1500 | 25 Oct 09 | 23:18 | 0.0285 | Scheduled Sample |
| 1600 | 26 Oct 09 | 02:38 | 0.041 | Scheduled Sample |
| 1700 | 26 Oct 09 | 06:16 | 0.078 | Scheduled Sample |
| 1800 | 26 Oct 09 | 09:55 | 0.1008 | Scheduled Sample |
| 1900 | 26 Oct 09 | 13:02 | 0.031 | Scheduled Sample |
| 1980 | 26 Oct 09 | 15:33 | 0.0359 | Scheduled Sample |
| 2000 | 26 Oct 09 | 16:08 | 0.040 | Scheduled Sample |
| 2050 | 26 Oct 09 | 17:28 | 0.0382 | Scheduled Sample |
| 2100 | 26 Oct 09 | 18:41 | 0.0505 | Scheduled Sample |
| 2150 | 26 Oct 09 | 20:14 | 0.0522 | Scheduled Sample |
| 2200 | 26 Oct 09 | 22:08 | 0.0514 | Scheduled Sample |
| 2250 | 26 Oct 09 | 22:43 | 0.040 | Scheduled Sample |
| 2300 | 27 Oct 09 | 01:27 | 0.042 | Scheduled Sample |
| 2350 | 27 Oct 09 | 03:17 | 0.120 | Scheduled Sample |
| 2400 | 27 Oct 09 | 04:53 | 0.160 | Scheduled Sample |
| 2450 | 27 Oct 09 | 05:21 | 0.170 | Scheduled Sample |
| 2500 | 27 Oct 09 | 07:52 | 0.130 | Scheduled Sample |
| 2550 | 27 Oct 09 | 09:29 | 0.180 | Scheduled Sample |
| 2600 | 27 Oct 09 | 11:09 | 0.130 | Scheduled Sample |
| 2650 | 27 Oct 09 | 12:40 | 0.1285 | Scheduled Sample |
| 2700 | 27 Oct 09 | 14:44 | 0.1190 | Scheduled Sample |
| 2750 | 27 Oct 09 | 16:06 | 0.110 | Scheduled Sample |
| 2800 | 27 Oct 09 | 18:13 | 0.090 | Scheduled Sample |
| 2815 | 27 Oct 09 | 18:57 | 0.1131 | Scheduled Sample |
| 2820 | 27 Oct 09 | 19:10 | 0.1443 | Scheduled Sample |
| 2830 | 27 Oct 09 | 19:46 | 0.4673 | Scheduled Sample |
| 2840 | 27 Oct 09 | 20:04 | 1.2166 | Scheduled Sample |
| 2850 | 27 Oct 09 | 20:35 | 0.3151 | Scheduled Sample |
| 2855 | 27 Oct 09 | 20:48 | 2.80 | Gas Peak |
| 2860 | 27 Oct 09 | 20:48 | 1.37 | Scheduled Sample |
| 2870 | 27 Oct 09 | 21:20 | 1.49 | Scheduled Sample |
| 2880 | 28 Oct 09 | 00:35 | 0.044 | Scheduled Sample |