| Date: | 28 Oct 2009 | Report Number: | 12 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 2912 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 2912 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 0 m | FIT: | 1.7 sg |
| Lag Depth: | 2889 mMDRT | Mud Weight: | 1.5 sg |
| Water Depth: | 503.0 m LAT | ECD: | N/A |
| RT: | 21.5 m | Mud Type: | Ultradrill / Kill mud |
| Last Survey Depth: | 2863.33 mMDRT | Mud Chlorides: | 52,000 |
| Deviation: | Inc 1.15° Azi 160.56° | Est. Pore Press: | > 1.5 sg EMW @ 2912 mMDRT |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | BOPs closed in on well kick. Circulated well to kill weight fluid. |
| --- | --- |
| NEXT 24 HOURS: | Continue well kill operations. |
| MIDNIGHT TO 0600hrs SUMMARY: | Continued well kill operations. |
| CURRENT OPERATION @ 06:00hrs: | Monitor well pressure with well closed in. |

## GEOLOGICAL SUMMARY

LITHOLOGY

# No new lithology drilled

HYDROCARBON FLUORESCENCE

# No hydrocarbon fluorescence.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2878 – 2899 | 0.037 | 0.0247 | 0.0007 | 0.0004 | 0 | 0 | 0 | 0 |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| 2886.76 (CO2) | 24.7 |  |  |  |  |  |  |  |
| 2886.93 | 2.45 | 2.2546 | 0.0534 | 0.0211 | 0.0020 | 0.0026 | 0.0007 | 0.0003 |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | Well displaced with 1.5 sg kill mud |
| Connection gas | Nil |
| Trip gas | Nil |
| Background gas | Background gas increased at top Thylacine Member from 2817 mMDRT. |
| Dxc exponent | Minor cutback at 1650 mMDRT. No other cut backs observed. |
| ROP | N/A |
| Ditch cuttings | No splintery or pressure style cavings observed. |
| Mud temperature out | No indication of overpressure. |
| MWD resistivity | The resistivity generated pore pressure trends were below or approaching the static mud weight from 2280 to 2470 mMDRT. From 2250 to 2295 and 2500 to 2520 mMDRT the static mud weight and resistivity generated pore pressure trends were approaching balance. Resistivity generated pore pressure trends were just above the static mud weight from 2480 to 2500 mMDRT. From ~2540 to 2730 mMDRT the resistivity generated pore pressure was greater than the static mud weight and was on average calculated to be 1.32 to 1.38 sg. |
| Pore Pressure Estimate | Maximum 1.38 sg EMW at ~2655 mMDRT (resistivity generated pore pressure estimate from town support). From 2745 to 2820 mMDRT the resistivity derived pore pressure estimate was below the static mud weight. From 2820 mMDRT no further pore pressure estimates were provided by town support. Influx shows bottom hole pore pressure is > 1.5 sg EMW. |

# SAMPLE QUALITY

# No cuttings returns were observed after 2878 mMDRT, at which point the well was shut-in to monitor well flow.  Very slow circulation rates (pump rate – 14 SPM) were established again.  Mud flow was regained albeit with no cuttings return.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All equipment operating and functional.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: All equipment functioned ok during drilling operations. At 00:00 hours 29th October 2009 SLB MWD estimate that 20% battery life is remaining.

| Sensor | Distance from Bit (m) |
| --- | --- |
| Pressure (Arc) | 9.31 |
| Resistivity(Arc) | 10.03 |
| Gamma Ray (Arc) | 10.08 |
| Vibration (TeleScope) | 17.05 |
| Direction & Inclination (TeleScope) | 18.05 |
| Delta T (sonic) | 27.56 |
| Ultrasonic (sADN) | 33.34 |
| Density (sADN) | 33.51 |
| Neutron (sADN) | 35.49 |

###### WIRELINE

Personnel: 7 x wireline crew on board.

Equipment: Wireline crew have successfully tested FMI, Neutron, PEX, HLA, Sonic and Spectral GR tools for success case run 1. The free point indicator tool, back-off tool and pipe severing tool were also checked.  The MDT tool is currently being checked whilst the mechanical sidewall coring tool remains to be checked.

REMARKS

CO2 gas peaked at 24.7% whilst circulating kill mud at 2886.76 mMDRT (17:30 hours 28th October 2009).

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 | 1330 | 1329.93 | 1308.43 | -1.57 | LWD |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 | 1602 | 1601.92 | 1580.42 | -1.58 | LWD / Cuttings |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 | 1680 | 1679.92 | 1658.42 | +21.42 | LWD / Cuttings |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 | 1732 | 1731.92 | 1710.42 | +23.42 | LWD / Cuttings |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 | 2140 | 2139.10 | 2117.60 | +33.60 | LWD |
| Thylacine Member |  | 2854 | 2832.5 | 100 | 2817 | 2816.7 | 2795.2 | -37.3 | GR cut back / cuttings |
| Flaxman Formation |  | 2880 | 2858.5 | 180 |  |  |  |  |  |
| Waare Formation |  | 3139 | 3117.5 | 50 |  |  |  |  |  |
| Eumeralla Formation |  | 3261 | 3239.5 | 70 |  |  |  |  |  |
| TD |  | 3311 | 3289.5 | 70 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| 2260 – 2810 | 10 | None |
| 2810 - 2875 | 5 | None |
| 2875 – 2878 | 3 | None |
| 2878 – 2899 | N/A | No cuttings sample returns |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| 1289 | Mud |
| 1289 | Filtrate |
| 2427 | Mud (Tracer added) |
| 2427 | Filtrate |
| 2820 | Mud (Reservoir) |
| 2820 | Filtrate (Reservoir) |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| 1300 | 25 Oct 09 | 17:08 | 0.0065 | Scheduled Sample |
| 1400 | 25 Oct 09 | 20:31 | 0.0162 | Scheduled Sample |
| 1500 | 25 Oct 09 | 23:18 | 0.0285 | Scheduled Sample |
| 1600 | 26 Oct 09 | 02:38 | 0.041 | Scheduled Sample |
| 1700 | 26 Oct 09 | 06:16 | 0.078 | Scheduled Sample |
| 1800 | 26 Oct 09 | 09:55 | 0.1008 | Scheduled Sample |
| 1900 | 26 Oct 09 | 13:02 | 0.031 | Scheduled Sample |
| 1980 | 26 Oct 09 | 15:33 | 0.0359 | Scheduled Sample |
| 2000 | 26 Oct 09 | 16:08 | 0.040 | Scheduled Sample |
| 2050 | 26 Oct 09 | 17:28 | 0.0382 | Scheduled Sample |
| 2100 | 26 Oct 09 | 18:41 | 0.0505 | Scheduled Sample |
| 2150 | 26 Oct 09 | 20:14 | 0.0522 | Scheduled Sample |
| 2200 | 26 Oct 09 | 22:08 | 0.0514 | Scheduled Sample |
| 2250 | 26 Oct 09 | 22:43 | 0.040 | Scheduled Sample |
| 2300 | 27 Oct 09 | 01:27 | 0.042 | Scheduled Sample |
| 2350 | 27 Oct 09 | 03:17 | 0.120 | Scheduled Sample |
| 2400 | 27 Oct 09 | 04:53 | 0.160 | Scheduled Sample |
| 2450 | 27 Oct 09 | 05:21 | 0.170 | Scheduled Sample |
| 2500 | 27 Oct 09 | 07:52 | 0.130 | Scheduled Sample |
| 2550 | 27 Oct 09 | 09:29 | 0.180 | Scheduled Sample |
| 2600 | 27 Oct 09 | 11:09 | 0.130 | Scheduled Sample |
| 2650 | 27 Oct 09 | 12:40 | 0.1285 | Scheduled Sample |
| 2700 | 27 Oct 09 | 14:44 | 0.1190 | Scheduled Sample |
| 2750 | 27 Oct 09 | 16:06 | 0.110 | Scheduled Sample |
| 2800 | 27 Oct 09 | 18:13 | 0.090 | Scheduled Sample |
| 2815 | 27 Oct 09 | 18:57 | 0.1131 | Scheduled Sample |
| 2820 | 27 Oct 09 | 19:10 | 0.1443 | Scheduled Sample |
| 2830 | 27 Oct 09 | 19:46 | 0.4673 | Scheduled Sample |
| 2840 | 27 Oct 09 | 20:04 | 1.2166 | Scheduled Sample |
| 2850 | 27 Oct 09 | 20:35 | 0.3151 | Scheduled Sample |
| 2855 | 27 Oct 09 | 20:48 | 2.80 | Gas Peak |
| 2860 | 27 Oct 09 | 20:48 | 1.37 | Scheduled Sample |
| 2870 | 27 Oct 09 | 21:20 | 1.49 | Scheduled Sample |
| 2880 | 28 Oct 09 | 00:35 | 0.044 | Scheduled Sample |
| 2881.6 | 28 Oct 09 | 08:10 | 0.203 | Bleed of choke line |
| 2881.6 | 28 Oct 09 | 08:24 | 1.160 | Bleed of choke line |
| 2885.4 | 28 Oct 09 | 16:48 | 1.94 | Circ. with kill mud |
| 2889.5 | 28 Oct 09 | 19:10 | 1.04 | Circ. with kill mud |