| Date: | 30 Oct 2009 | Report Number: | 14 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 2912 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 2912 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 0 m | FIT: | 1.7 sg |
| Lag Depth: | 2878 mMDRT | Mud Weight: | 1.58 sg |
| Water Depth: | 503.0 m LAT | ECD: | N/A |
| RT: | 21.5 m | Mud Type: | Ultradrill / Kill mud |
| Last Survey Depth: | 2863.33 mMDRT | Mud Chlorides: | 45,000 |
| Deviation: | Inc 1.15° Azi 160.56° | Est. Pore Press: | 1.38sg EMW @ ~2655 mMDRT |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Completed circulating well to 1.5sg (12.5ppg) kill weight mud. Shut in choke and monitored pressures. Circulated well to 1.58sg (13.2ppg) kill weight mud. Shut in choke and monitored pressures. |
| --- | --- |
| NEXT 24 HOURS: | Complete riser displacement. Lubricate fluids under annular BOP. Open BOPs and circulate hole clean. |
| MIDNIGHT TO 0600hrs SUMMARY: | Attempted to bleed 7.9m3 (50bbls) from choke. Total volume returned after 1hr = 0.5m3 (3bbls). Shut in choke and monitored pressures. Lined up to displace riser to 1.58sg (13.2ppg) mud. Displaced riser to 1.58sg (13.2ppg) mud. |
| CURRENT OPERATION @ 06:00hrs: | Displacing riser to 1.58sg (13.2ppg) kill weight mud. |

## GEOLOGICAL SUMMARY

LITHOLOGY

No new formation drilled.

HYDROCARBON FLUORESCENCE

# No hydrocarbon fluorescence.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N/A | - | - | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.58 sg |
| Connection gas | Nil |
| Trip gas | Nil |
| Background gas | Background gas increased at top Thylacine Member from 2817 mMDRT. |
| Dxc exponent | Minor cutback at 1650 mMDRT. No other cut backs observed. |
| ROP | N/A |
| Ditch cuttings | No splintery or pressure style cavings observed. |
| Mud temperature out | No indication of overpressure. |
| MWD resistivity | The resistivity generated pore pressure trends were below or approaching the static mud weight from 2280 to 2470 mMDRT. From 2250 to 2295 and 2500 to 2520 mMDRT the static mud weight and resistivity generated pore pressure trends were approaching balance. Resistivity generated pore pressure trends were just above the static mud weight from 2480 to 2500 mMDRT. From ~2540 to 2730 mMDRT the resistivity generated pore pressure was greater than the static mud weight and was on average calculated to be 1.32 to 1.38 sg. |
| Pore Pressure Estimate | Maximum 1.38 sg EMW at ~2655 mMDRT (resistivity generated pore pressure estimate from town support). From 2745 to 2820 mMDRT the resistivity derived pore pressure estimate was below the static mud weight. From 2820 mMDRT no further pore pressure estimates were provided by town support. |

# SAMPLE QUALITY

# No cuttings returned. Bagged samples to date are still drying.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All equipment operating and functional.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: All equipment functioned well during drilling operations. Batteries are expected to be fully depleted at present.

| Sensor | Distance from Bit (m) |
| --- | --- |
| Pressure (Arc) | 9.31 |
| Resistivity(Arc) | 10.03 |
| Gamma Ray (Arc) | 10.08 |
| Vibration (TeleScope) | 17.05 |
| Direction & Inclination (TeleScope) | 18.05 |
| Delta T (sonic) | 27.56 |
| Ultrasonic (sADN) | 33.34 |
| Density (sADN) | 33.51 |
| Neutron (sADN) | 35.49 |

###### WIRELINE

Personnel: 3x wireline crew on board.

Equipment: All surplus tools have been packed into their relevant baskets and off-loaded to the boat.

REMARKS

None

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 | 1330 | 1329.93 | 1308.43 | -1.57 | LWD |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 | 1602 | 1601.92 | 1580.42 | -1.58 | LWD / Cuttings |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 | 1680 | 1679.92 | 1658.42 | +21.42 | LWD / Cuttings |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 | 1732 | 1731.92 | 1710.42 | +23.42 | LWD / Cuttings |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 | 2140 | 2139.10 | 2117.60 | +33.60 | LWD |
| Thylacine Member |  | 2854 | 2832.5 | 100 | 2817 | 2816.7 | 2795.2 | -37.3 | GR cut back / cuttings |
| Flaxman Formation |  | 2880 | 2858.5 | 180 |  |  |  |  |  |
| Waare Formation |  | 3139 | 3117.5 | 50 |  |  |  |  |  |
| Eumeralla Formation |  | 3261 | 3239.5 | 70 |  |  |  |  |  |
| TD |  | 3311 | 3289.5 | 70 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| 2260 – 2810 | 10 | None |
| 2810 - 2875 | 5 | None |
| 2875 – 2878 | 3 | None |
| 2878 – 2912 | N/A | No cuttings sample returns |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| 1289 | Mud |
| 1289 | Filtrate |
| 2427 | Mud (Tracer added) |
| 2427 | Filtrate |
| 2820 | Mud (Reservoir) |
| 2820 | Filtrate (Reservoir) |
| 2900 | Mud |
| 2900 | Filtrate |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| 1300 | 25 Oct 09 | 17:08 | 0.0065 | Scheduled Sample |
| 1400 | 25 Oct 09 | 20:31 | 0.0162 | Scheduled Sample |
| 1500 | 25 Oct 09 | 23:18 | 0.0285 | Scheduled Sample |
| 1600 | 26 Oct 09 | 02:38 | 0.041 | Scheduled Sample |
| 1700 | 26 Oct 09 | 06:16 | 0.078 | Scheduled Sample |
| 1800 | 26 Oct 09 | 09:55 | 0.1008 | Scheduled Sample |
| 1900 | 26 Oct 09 | 13:02 | 0.031 | Scheduled Sample |
| 1980 | 26 Oct 09 | 15:33 | 0.0359 | Scheduled Sample |
| 2000 | 26 Oct 09 | 16:08 | 0.040 | Scheduled Sample |
| 2050 | 26 Oct 09 | 17:28 | 0.0382 | Scheduled Sample |
| 2100 | 26 Oct 09 | 18:41 | 0.0505 | Scheduled Sample |
| 2150 | 26 Oct 09 | 20:14 | 0.0522 | Scheduled Sample |
| 2200 | 26 Oct 09 | 22:08 | 0.0514 | Scheduled Sample |
| 2250 | 26 Oct 09 | 22:43 | 0.040 | Scheduled Sample |
| 2300 | 27 Oct 09 | 01:27 | 0.042 | Scheduled Sample |
| 2350 | 27 Oct 09 | 03:17 | 0.120 | Scheduled Sample |
| 2400 | 27 Oct 09 | 04:53 | 0.160 | Scheduled Sample |
| 2450 | 27 Oct 09 | 05:21 | 0.170 | Scheduled Sample |
| 2500 | 27 Oct 09 | 07:52 | 0.130 | Scheduled Sample |
| 2550 | 27 Oct 09 | 09:29 | 0.180 | Scheduled Sample |
| 2600 | 27 Oct 09 | 11:09 | 0.130 | Scheduled Sample |
| 2650 | 27 Oct 09 | 12:40 | 0.1285 | Scheduled Sample |
| 2700 | 27 Oct 09 | 14:44 | 0.1190 | Scheduled Sample |
| 2750 | 27 Oct 09 | 16:06 | 0.110 | Scheduled Sample |
| 2800 | 27 Oct 09 | 18:13 | 0.090 | Scheduled Sample |
| 2815 | 27 Oct 09 | 18:57 | 0.1131 | Scheduled Sample |
| 2820 | 27 Oct 09 | 19:10 | 0.1443 | Scheduled Sample |
| 2830 | 27 Oct 09 | 19:46 | 0.4673 | Scheduled Sample |
| 2840 | 27 Oct 09 | 20:04 | 1.2166 | Scheduled Sample |
| 2850 | 27 Oct 09 | 20:35 | 0.3151 | Scheduled Sample |
| 2855 | 27 Oct 09 | 20:48 | 2.80 | Gas Peak |
| 2860 | 27 Oct 09 | 20:48 | 1.37 | Scheduled Sample |
| 2870 | 27 Oct 09 | 21:20 | 1.49 | Scheduled Sample |
| 2880 | 28 Oct 09 | 00:35 | 0.044 | Scheduled Sample |
| 2881.6 | 28 Oct 09 | 08:10 | 0.203 | Bleed of choke line |
| 2881.6 | 28 Oct 09 | 08:24 | 1.160 | Bleed of choke line |
| 2885.4 | 28 Oct 09 | 16:48 | 1.94 | Circ. with kill mud |
| 2890 | 28 Oct 09 | 19:10 | 1.04 | Circ. with kill mud |
| 2900 | 29 Oct 09 | 04:15 | 0.03 | Circ. with kill mud |