| Date: | 02 Nov 2009 | Report Number: | 17 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 2912 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 2912 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 0 m | FIT: | 1.7 sg |
| Lag Depth: | 2878 mMDRT | Mud Weight: | 1.7 sg |
| Water Depth: | 503.0 m LAT | ECD: | N/A |
| RT: | 21.5 m | Mud Type: | Ultradrill / Kill mud |
| Last Survey Depth: | 2863.33 mMDRT | Mud Chlorides: | 38,000 |
| Deviation: | Inc 1.15° Azi 160.56° | Est. Pore Press: | 1.38sg EMW @ ~2655 mMDRT > 1.50 sg EMW @ ~2912 mMDRT |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Completed pumping out of hole. Experienced major losses below the shoe. Re-established circulation with 1.58 sg (13.2 ppg) mud down riser booster line while simultaneously filing with sea water. Racked back the 311 mm (12.25”) BHA in the derrick. RIH to shoe with 127 mm (5”) drill pipe. |
| --- | --- |
| NEXT 24 HOURS: | Plug and abandon well. |
| MIDNIGHT TO 0600hrs SUMMARY: | POOH with 127 mm (5”) HWDP and laid out same. RIH with 127 mm (5”) DP from 1103 to 1247 mMDRT. Waited on barite from the Lewek Emerald support vessel. Pumped an LCM pill. POOH from 1247 to 1103 mMDRT to above the LCM pill. Continued to wait on barite from the Lewek Emerald support vessel. Prepared for cementing operations. |
| CURRENT OPERATION @ 06:00hrs: | Waiting on weather, unable to receive barite from the Lewek Emerald support vessel. |

## GEOLOGICAL SUMMARY

LITHOLOGY

No new formation drilled.

HYDROCARBON FLUORESCENCE

# No hydrocarbon fluorescence.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N/A | - | - | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| None | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.7 sg |
| Connection gas | Nil |
| Trip gas | Nil |
| Background gas | Background gas increased at top Thylacine Member from 2817 mMDRT. |
| Dxc exponent | Minor cutback at 1650 mMDRT. No other cut backs observed. |
| ROP | N/A |
| Ditch cuttings | No splintery or pressure style cavings observed. |
| Mud temperature out | No indication of overpressure. |
| MWD resistivity | The resistivity generated pore pressure trends were below or approaching the static mud weight from 2280 to 2470 mMDRT. From 2250 to 2295 and 2500 to 2520 mMDRT the static mud weight and resistivity generated pore pressure trends were approaching balance. Resistivity generated pore pressure trends were just above the static mud weight from 2480 to 2500 mMDRT. From ~2540 to 2730 mMDRT the resistivity generated pore pressure was greater than the static mud weight and was on average calculated to be 1.32 to 1.38 sg. |
| Pore Pressure Estimate | Maximum 1.38 sg EMW at ~2655 mMDRT (resistivity generated pore pressure estimate from town support). From 2745 to 2820 mMDRT the resistivity derived pore pressure estimate was below the static mud weight. From 2820 mMDRT no further pore pressure estimates were provided by town support. Influx shows bottom hole pore pressure is > 1.5 sg EMW. |

# SAMPLE QUALITY

# Bagged samples are packed up and ready to be shipped to town where they will be split.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 2x Mudloggers. 2x Mudloggers are schedule to depart the rig on 3rd November 2009.

Equipment: All equipment operating and functional.

### MWD/LWD

Personnel:  3x LWD Engineers.

REMARKS

This is the final Daily Geological Report for Somerset-1.

### WELLSITE GEOLOGISTS

David Hartney

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 | 1330 | 1329.93 | 1308.43 | -1.57 | LWD |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 | 1602 | 1601.92 | 1580.42 | -1.58 | LWD / Cuttings |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 | 1680 | 1679.92 | 1658.42 | +21.42 | LWD / Cuttings |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 | 1732 | 1731.92 | 1710.42 | +23.42 | LWD / Cuttings |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 | 2140 | 2139.10 | 2117.60 | +33.60 | LWD |
| Thylacine Member |  | 2854 | 2832.5 | 100 | 2817 | 2816.7 | 2795.2 | -37.3 | GR cut back / cuttings |
| Flaxman Formation |  | 2880 | 2858.5 | 180 |  |  |  |  |  |
| Waare Formation |  | 3139 | 3117.5 | 50 |  |  |  |  |  |
| Eumeralla Formation |  | 3261 | 3239.5 | 70 |  |  |  |  |  |
| TD |  | 3311 | 3289.5 | 70 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD | 2912.0 | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| 2260 – 2810 | 10 | None |
| 2810 - 2875 | 5 | None |
| 2875 – 2878 | 3 | None |
| 2878 – 2912 | N/A | No cuttings sample returns |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| 1289 | Mud |
| 1289 | Filtrate |
| 2427 | Mud (Tracer added) |
| 2427 | Filtrate |
| 2820 | Mud (Reservoir) |
| 2820 | Filtrate (Reservoir) |
| 2900 | Mud |
| 2900 | Filtrate |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| 1300 | 25 Oct 09 | 17:08 | 0.0065 | Scheduled Sample |
| 1400 | 25 Oct 09 | 20:31 | 0.0162 | Scheduled Sample |
| 1500 | 25 Oct 09 | 23:18 | 0.0285 | Scheduled Sample |
| 1600 | 26 Oct 09 | 02:38 | 0.041 | Scheduled Sample |
| 1700 | 26 Oct 09 | 06:16 | 0.078 | Scheduled Sample |
| 1800 | 26 Oct 09 | 09:55 | 0.1008 | Scheduled Sample |
| 1900 | 26 Oct 09 | 13:02 | 0.031 | Scheduled Sample |
| 1980 | 26 Oct 09 | 15:33 | 0.0359 | Scheduled Sample |
| 2000 | 26 Oct 09 | 16:08 | 0.040 | Scheduled Sample |
| 2050 | 26 Oct 09 | 17:28 | 0.0382 | Scheduled Sample |
| 2100 | 26 Oct 09 | 18:41 | 0.0505 | Scheduled Sample |
| 2150 | 26 Oct 09 | 20:14 | 0.0522 | Scheduled Sample |
| 2200 | 26 Oct 09 | 22:08 | 0.0514 | Scheduled Sample |
| 2250 | 26 Oct 09 | 22:43 | 0.040 | Scheduled Sample |
| 2300 | 27 Oct 09 | 01:27 | 0.042 | Scheduled Sample |
| 2350 | 27 Oct 09 | 03:17 | 0.120 | Scheduled Sample |
| 2400 | 27 Oct 09 | 04:53 | 0.160 | Scheduled Sample |
| 2450 | 27 Oct 09 | 05:21 | 0.170 | Scheduled Sample |
| 2500 | 27 Oct 09 | 07:52 | 0.130 | Scheduled Sample |
| 2550 | 27 Oct 09 | 09:29 | 0.180 | Scheduled Sample |
| 2600 | 27 Oct 09 | 11:09 | 0.130 | Scheduled Sample |
| 2650 | 27 Oct 09 | 12:40 | 0.1285 | Scheduled Sample |
| 2700 | 27 Oct 09 | 14:44 | 0.1190 | Scheduled Sample |
| 2750 | 27 Oct 09 | 16:06 | 0.110 | Scheduled Sample |
| 2800 | 27 Oct 09 | 18:13 | 0.090 | Scheduled Sample |
| 2815 | 27 Oct 09 | 18:57 | 0.1131 | Scheduled Sample |
| 2820 | 27 Oct 09 | 19:10 | 0.1443 | Scheduled Sample |
| 2830 | 27 Oct 09 | 19:46 | 0.4673 | Scheduled Sample |
| 2840 | 27 Oct 09 | 20:04 | 1.2166 | Scheduled Sample |
| 2850 | 27 Oct 09 | 20:35 | 0.3151 | Scheduled Sample |
| 2855 | 27 Oct 09 | 20:48 | 2.80 | Gas Peak |
| 2860 | 27 Oct 09 | 20:48 | 1.37 | Scheduled Sample |
| 2870 | 27 Oct 09 | 21:20 | 1.49 | Scheduled Sample |
| 2880 | 28 Oct 09 | 00:35 | 0.044 | Scheduled Sample |
| 2881.6 | 28 Oct 09 | 08:10 | 0.203 | Bleed of choke line |
| 2881.6 | 28 Oct 09 | 08:24 | 1.160 | Bleed of choke line |
| 2885.4 | 28 Oct 09 | 16:48 | 1.94 | Circ. with kill mud |
| 2890 | 28 Oct 09 | 19:10 | 1.04 | Circ. with kill mud |
| 2900 | 29 Oct 09 | 04:15 | 0.03 | Circ. with kill mud |