Report for : Dan Daniels / Mark Calicutt  / Andy Choy

Compiled by : Gareth Munro / Dan Dennis

| WELL | WKF W12A |
| --- | --- |
| DATE | 24-11-2009 |
| REPORT # | 7 |
| MIDNIGHT ACTIVITY | Pump out of hole |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2440.00 mMDRT |  | MINIMUM | 14.47 | 2344.5 |
| TVD | 2422.17 mTVDRT |  | MAXIMUM | 62.55 | 2436.5 |
| PROGRESS LAST 24 hrs | 181.0 m |  | AVERAGE | 38.51 | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 1488.0 | 1474.0 | -1432.3 | 2.3L | 1483.5 | 1471.7 |
| Top of Lakes Entrance Formation | 1885.0 | 1867.4 | -1825.7 | -5.3H | 1888.7 | 1872.7 |
| Top of Latrobe Group | 2283.5 | 2265.7 | -2224.0 | 4.0L | 2278.0 | 2261.7 |
| Top Coarse Clastics (SBP2) | 2304.0 | 2286.2 | -2244.5 | 0.5L | 2302.0 | 2285.7 |
| Top Up. M diversus | 2304.0 | 2286.2 | -2244.5 | 0.5L | 2302.0 | 2285.7 |
| Top M12 (PSB3) | 2312.0 | 2294.2 | -2252.5 | 2.5L | 2308.0 | 2291.7 |
| Top M13 (PSB7) | 2318.8 | 2301.0 | -2259.3 | -0.7H | 2318.0 | 2301.7 |
| Top M14 (SB13) | 2352.8 | 2335.0 | -2293.3 | 3.3L | 2348.0 | 2331.7 |
| Top M15 | 2368.8 | 2351.0 | -2309.3 | -0.7H | 2368.0 | 2351.7 |
| OOWC | 2371.5 | 2353.7 | -2312.0 | 0.0 | 2372.0 | 2353.7 |
| Total Depth | 2440.0 | 2422.17 | -2380.44 | 6.47L | 2432.98 | 2415.70 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2326.0 | 109.0 | 0.880 | 0.214 | 0.185 | 0.111 | 0.031 | - |
| MAX (GFF) | 2321.0 | 105.0 | 1.744 | 0.221 | 0.171 | 0.105 | 0.045 | - |
| BG (Reserval) | 2259.0 – 2440.0 | 35.9 | 0.294 | 0.071 | 0.059 | 0.040 | 0.013 | 0 |
| BG (GFF) | 2259.0 – 2440.0 | 25.9 | 0.268 | 0.054 | 0.050 | 0.040 | 0.020 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR516M-B6 |  |
| JETS (/32 inch) | 7 x 18 |  |
| DEPTH IN (m) | 637.0 |  |
| DEPTH OUT (m) | 2440.0 |  |
| METRES ON RUN (m) | 1803.0 |  |
| HRS ON BTM 24hrs/total | 4.7 / 32.0 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 90 – 141 |  |
| Pump Hrs 24 hrs / total | 15.7 / 66.3 |  |
| Krevs 24 hrs / total | 29.4 / 248.0 |  |

| 24 HOUR SUMMARY | Continue to drill 9-7/8” hole as per Schlumberger’s instruction from 2107.0 m to 2227.0 mMDRT. Commence control drilling at 50 m/hr to Total Depth at 2440.0 mMDRT. Back ream out of hole slowly, cleaning up hole, racking back a stand every 15 minutes back to 1876.0 mMDRT. Circulate and work pipe at 1876.0 mMDRT, with 2 full circulations until screen out Baracarb from mud (change shaker screens to API 230 mesh. Slug pipe and pull out of hole on elevators back to 1440.0 mMDRT where encountered 30 Klbs overpull. Run back in 2 stands then back ream out of hole. |
| --- | --- |
| 25-11-2009 5 AM UPDATE | Carefully pull BHA inside 10-3/4” shoe then circulate until shakers are clean. Slug pipe then pull out of hole on elevators, flow checking at the 5.5” HWDP. Layout radioactive sources. 2440.0 mMDRT (2422.17 mTVDRT) |