Report for : Greg Doty / Sam Falkner

Compiled by : Alex Djukanovic / Phil Rady

| WELL | WKF W8A |
| --- | --- |
| DATE | 10-12-2009 |
| REPORT # | 12 |
| MIDNIGHT ACTIVITY | Conduct safety stand down. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4535.00 m |  | MINIMUM | - | - |
| TVD | 2455.57 m |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 |  | AVERAGE | - |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2304.0 | 1378.4 | -1336.73 | -3.3H | 2310.0 | 1381.7 |
| Mid Miocene Marker | 3838.0 | 1843.9 | -1802.16 | 2.2L | 3840.0 | 1841.7 |
| Top of Lakes Entrance Formation | 3973.0 | 1933.6 | -1891.9 | -8.1H | 3940.0 | 1941.7 |
| Top of Latrobe Group | 4352.5 | 2274.2 | -2232.5 | 3.1L | 4352.0 | 2271.1 |
| Top P1.1 West | 4382.0 | 2303.7 | -2262.0 | 7.0L | 4378.0 | 2297.7 |
| Top Coarse Clastics (SBP3) | 4397.0 | 2318.7 | -2277.0 | 7.0L | 4392.0 | 2311.7 |
| Top M1.3U (PSB7) | 4416.0 | 2337.7 | -2296.0 | 2.0L | 4416.0 | 2335.7 |
| PSB5 | 4422.0 | 2343.7 | -2302.0 | 2.0L | 4422.0 | 2341.7 |
| PSB4 | 4427.0 | 2348.7 | -2307.0 | 3.0L | 4426.0 | 2345.7 |
| Top M1.4U (SB13) | 4435.0 | 2356.7 | -2315.0 | 2.0L | 4435.0 | 2354.7 |
| Top M1.4L | 4451.0 | 2372.7 | -2331.0 | 1.0L | 4452.0 | 2371.7 |
| M1.4C | 4458.0 | 2379.7 | -2338.0 | 2.0L | 4458.0 | 2377.7 |
| M1.4C OOWC | 4459.0 | 2380.7 | -2339.0 | 1.2L | 4459.0 | 2379.5 |
| Top M1.5 | 4466.0 | 2387.7 | -2346.0 | 0.0 | 4468.0 | 2387.7 |
| M1.4B OOWC | 4472.0 | 2393.7 | -2352.0 | 5.3L | 4469.0 | 2388.4 |
| Total Depth | 4535.0 | 2455.57 | -2413.87 | 7.27L | 4529.0 | 2448.3 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. |  |  |
| SIZE (in) |  |  |
| MANUFACTURER/TYPE |  |  |
| JETS (/32 inch) |  |  |
| DEPTH IN (m) |  |  |
| DEPTH OUT (m) |  |  |
| METRES ON RUN (m) |  |  |
| HRS ON BTM 24hrs/total |  |  |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs |  |  |
| Pump Hrs 24 hrs / total |  |  |
| Krevs 24 hrs / total |  |  |

| 24 HOUR SUMMARY | Continue Hazard Hunt. Trip in hole. JSA conducted. Continue to make up diffuser tool and pick up 4” drill pipe from V-door and run in hole to 290m. Continue to run in hole from derrik with 4” drill pipe from 290m to 498m. Trip in hole change out to 5 ½” handling gear. Make up crossover and run in hole from derrik with 5 ½” drill pipe from 498m to casing shoe at 898m. Continue to run in hole from 828m to 2489m. |
| --- | --- |
| 10-12-2009 5 AM UPDATE | Continue to run in hole with 5 ½” drill pipe on 4” drill pipe Cement stinger BHA from 2489m to 4527m. Make up top drive and wash down to tag with 10K at 4535m. Circulating and conditioning mud while working pipe. Held pre cement job JSA whilst conditioning the mud. Make up drop ball cement assembly. Rig up high pressure hoses required for job. Break circulation and pump 20bbls of 12.5ppg tuned spacer with rig. HOWCO pressure test lines to 300/3000psi for 5 minutes – test ok. Drop ball and mix and pump 67bbls of 15.8ppg slurry at 4535m as per program. Flush cement from lines and switch over to rig. Rig displaces 286bbls of mud as per cement procedure. Lay out cement assembly and pull out of hole racking back 5 ½” drill pipe in the derrik. 4535.0 mMDRT (2455.57 mTVDRT) |