LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 15 | DFS: | 15 | DATE : | 31-10-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1,448 | LAST DEPTH : | 1378 | 24 HR PROGRESS: | 70 | PTD : |  |
| TOTAL FUEL : | 8,500 | FUEL USAGE : | 1,250 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled to 1478m-circ-survey Tripping out for DST # 1 |
| Next 24 Hrs Op | Trip in hole – DST –POH DST Tools –RIH with Bit to drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 5 |  |  | Drilling | 5.00 |  | Density | 1.200 | S.G. |
| Size (mm) | 156 |  |  | Tripping | 9.50 |  | Viscosity | 42 | Sec |
| Make | Smith |  |  | Surveys |  |  | Water Loss |  | Cc |
| Type | MDi613 |  |  | Wireline logging |  |  | pH | 9.5 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 2 | 32 nd |
| Serial Number | JD1042 |  |  | Circulate Sample |  |  | PV / YP | 10/ 22 | Cp/lb/100’ |
| Nozzles (32) | 3 x 12 |  |  | Casing |  |  | Gels | 4 / 7 | S/m |
| Depth in (m) | 1378 |  |  | Cementing |  |  | Sand | 0.40 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 9.5 | % Vol |
| Total Metres | 70 |  |  | Circulate & Condition | 1.50 |  | Oil |  | % Vol |
| Hours | 5 |  |  | Rig Service/slip & cut | 1.00 |  | K+ |  | Mg/l |
| WOB (kg) | 2,000 |  |  | Rig up/ d own bop |  |  | Chlorides | 16,800 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt | 2.00 |  | PHPA |  |  |
| Condition | S.I.H |  |  | Reaming |  |  | KCL | 1.8 | % |
| Impact Force | 257 |  |  | Wait On Cement |  |  | Daily Cost $ | 8,567 |
| Jet Velocity | 219 |  |  | Test BOPs | 5.00 |  | Cum Cost $ | 47,165 |
| B.H.A.: 5 | 156mm Bit-NBS with Float and Totco ring on top of NBS-NMDC-Stab-2 x 4¾" DC-STB-12 x 4¾" DC-Jars-2 x 4¾" DC |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 03.30 | Completed the testing of BOP –Choke manifold |  |  | ° at |  | m |  | AMC Biocide G | 2 |
| 03.30 | 04.30 | Slipped block line |  |  | ° at |  | m |  | Xan- Bore | 2 |
| 04.30 | 11.00 | Picked up new 156mm BHA tripped in hole to 536m |  |  | ° at |  | m |  | Barytes | 240 |
| 11.00 | 12.00 | Tested 3½" pipe rams and Annular used Halliburton |  |  | ° at |  | m |  | Barite Lakes | 76 |
| 12.00 | 13.30 | Continued trip in hole to 1012m |  |  | ° at |  | m |  | Potassium Chloride | 9 |
| 13.00 | 14,00 | Circulated to mud |  |  | ° at |  | m |  | Residrill | 62 |
| 14.00 | 15.00 | Continued trip in hole to 1357m |  |  | ° at |  | m |  |  |  |
| 15.00 | 16.00 | Layed out excess drill pipe then picked up the Kelly |  |  |  |  |
| 16.00 | 18.00 | Drilled out shoetrack |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 18.00 | 18.30 | Drilled 3m new hole from 1378m to 1381m |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 18.30 | 19.00 | Circulated mud to 9.8ppg all round |  | Pressure |  | kPa |  | Pressure | 7,700 | KPa |
| 19.00 | 19.30 | Performed P.I.T test to 775psi |  | A.V. DP |  | m/min |  | A.V. DP | 220 | Ft/min |
| 19.30 | 24.00 | Drilled 156mm hole from 1381m to 1448m |  | A.V. DC |  | m/min |  | A.V. DC | 371 | Ft//mn |
|  |  |  |  | SPM |  |  | SPM | 100 |
|  |  |  |  | LPM |  |  | GPM | 227 |
|  |  | Held BOP drill on connection |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  |  |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 117 |  |
|  |  |  |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66