LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 37 | DFS: | 37 | DATE : | 22-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 7,400 | FUEL USAGE : | 900 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Finished trip out-Serviced tools -Tripped in hole with DST tools for 3rd test at 1171m-1174m interval -Slip block line at 06.00hrs |
| Next 24 Hrs Op | Re- Run the previous test with larger water cushion |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density | 1.200 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 37 | Sec |
| Make |  |  |  | Downtime ( Float ) |  |  | Water Loss | 22.0 | Cc |
| Type |  |  |  | Wireline logging |  |  | pH | 8.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 7 / 11 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels | 2 / 5 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.25 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing | 24 |  | Solids | 10.7 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 7,875 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 11,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | 1.5 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ |  |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 91,474 |
| B.H.A.: 5 |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 01.00 | Continued the flow test ( no surface flow ) Test # 1 |  |  | ° at |  | m |  | AMC Pac L |  |
| 01.00 | 01.30 | Unseated Packer –dropped bar –reversed out |  |  | ° at |  | m |  | AMC Pac R |  |
| 01.30 | 04.30 | Tripped out –drag from 1170m-1110m sand packed |  |  | ° at |  | m |  | Lakes Pac R |  |
| 04.30 | 11.00 | Serviced DST tools all sand blocked |  |  | ° at |  | m |  | Xan Bore | 2 |
| 11.00 | 14.30 | Tripped in hole with DST tools to 850m |  |  | ° at |  | m |  | Bayrtes | 220 |
| 14.30 | 15.30 | Ran water cushion in pipe string |  |  | ° at |  | m |  | Potassium Chloride |  |
| 15.30 | 16.30 | Continued trip in hole |  |  | ° at |  | m |  | AMC Biocide G |  |
| 16.30 | 17.00 | Made up and tested surface equipment |  |  |  |  |
| 17.00 | 17.30 | Set packers at 1170m-1175m perfs at 1171m-1174m |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 17.30 | 18.00 | Opened tools for test # 2 |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 18.00 | 18.30 | Close flow port |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 18.30 | 19.00 | Opened tools flowed well no surface flows visible |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
| 19.00 | 19.30 | Closed tool –deflated packers –dropped bar |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
| 19.30 | 20.00 | Reverse circulated –pumped pill |  | SPM |  |  | SPM |  |
| 20.00 | 20.30 | Rigged down surface tools |  | GPM |  |  | GPM |  |
| 20.30 | 24.00 | Tripped out to 70m ( Drag for first 5 stands) |  |  |  |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 18 camp 4 Schlumberger 3 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 2 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 2 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | 465 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66