LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 2 | DFS: | 2 | DATE : | 18-10-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 302m | LAST DEPTH : | 23m | 24 HR PROGRESS: | 279m | PTD : |  |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Rigging up for running 9⅝" Casing |
| Next 24 Hrs Op | Run casing –cement same – woc install 3 k BOP |
| Site Personnel: | Hunt Energy 18 Camp 4 Lakes Oil 3 RMN 1 Baker Mud Loggers 2 Halliburton 2 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-run |  |  | Drilling | 16.5 |  | Density | 9.2-9.5 1.104-1.14 | S.G. |
| Size (mm) | 311 |  |  | Tripping | 4.0 |  | Viscosity | 48-54 | Sec |
| Make | Reed |  |  | Slip Cut |  |  | Water Loss |  | Cc |
| Type | EPH41 HKPR |  |  | Rigged up |  |  | pH |  | Strip |
| IADC Code | 4-1-7 |  |  | Testing/tools |  |  | Filter Cake |  | 32 nd |
| Serial Number | NR 2008 |  |  | Circulate Sample |  |  | PV / YP |  | Cp/lb/100’ |
| Nozzles (32) | 18-18-18 |  |  | Casing |  |  | Gels |  | S/m |
| Depth in (m) | 16 |  |  | Cementing |  |  | Sand |  | % Vol |
| Depth out (m) | 302 |  |  | Surveys | 2.0 |  | Solids |  | % Vol |
| Total Metres | 285 |  |  | Circulate & Condition | 1.5 |  | Oil |  | % Vol |
| Hours | 18.5 |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 2000 |  |  | Rig down bop |  |  | Chlorides |  | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Breakdown kelly |  |  | KCL | % |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 1,172 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 3,866 |
| B.H.A.: | 311mm bit-NBS-8" DC-STB-8" DC-X/O-8 x 6¼" DC- Drilling Jar-3 x 6¼" DC-4 x HWDP- X/O |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | ¾º | ° at | 32 | m |  | Type | Amount |
| 00.00 | 01.00 | Drilled 311mm hole from 23m to 34m |  | ½º | ° at | 96 | m |  | Gel | 75 |
| 01.00 | 01.30 | Survey at 32m |  | 1º | ° at | 239 | m |  | Soda ash | 2 |
| 01.30 | 07.00 | Drilled 311mm hole from 34m to 99m |  | 1½º | ° at | 295 | m |  |  |  |
| 07.00 | 07.30 | Survey at 96m |  |  | ° at |  | m |  |  |  |
| 07.30 | 15.00 | Drilled 311mm hole from 99m to 249m |  |  | ° at |  | m |  |  |  |
| 15.00 | 15.30 | Survey at 239m |  |  | ° at |  | m |  |  |  |
| 15.30 | 18.00 | Drilled 311mm hole from 249m to 302m |  |  | ° at |  | m |  |  |  |
| 18.00 | 18.30 | Circulated hole clean |  |  |  |  |
| 18.30 | 19.00 | Survey at 295m |  | PUMP 1 |  | PUMP 2 |
| 19.00 | 20.30 | Wiper tripped back to 105m |  | Liner |  | mm |  | Liner |  | mm |
| 20.30 | 21.30 | Tripped back in hole to bottom at 302m no fill |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 21.30 | 22.30 | Circulated pumped carbide |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
| 22.30 | 24.00 | Tripped out for running casing |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 340 | mm |
|  |  | Water from Dyers 5 loads so far |  | Class Bulk |  |  | Weight | 79.45 | Kg/m |
|  |  | Transport Cost 2 Trailers Mud from Adelaide |  | % |  |  |  | Grade | K-55 |  |
|  |  | Transport Cost 2 Trailers of Casing |  | % |  |  |  | Connection | BTC |  |
|  |  | Transport Cost Hofco Equipment |  | % |  |  |  | Joints | 1 |  |
|  |  | Transport Cost Wood Group equipment |  | % |  |  |  | Length | 12.00 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 16m from RKB | m |

,66